Assignment 9 Solutions

- fact:

subu 	$sp, $sp, 32	# Allocate space for stack frame

sw		$ra, 20($sp)	# Save return address

sw		$fp, 16($sp)	# Save frame pointer

addiu	$fp, $sp, 28	# Set up frame pointer

sw		$a0, 0($fp)	# Save first argument (n)

bgtz	$a0, $L2	# Branch if n > 0

li		$v0, 1		# Return 1

jr		$L1		# Jump to return code

$L2:

lw		$v1, 0($fp)	# Load n

subu	$a0, $v1, 1	# Compute n – 1, store as first argument

jal		fact		# Call fact(n-1)

lw		$v1, 0($fp)	# Load n

mul	$v0, $v0, $v1	# Compute fact(n-1) * n

$L1:				# Code to return from function

lw		$ra, 20($sp)	# Restore ra

lw		$fp, 16($sp)	# Restore fp

addiu	$sp, $sp, 32	# Pop Stack

jr		$ra		# Return to caller

- Spim Assembly Program

.data

str:	.asciiz	“Enter a integer (or 0 to end): ”

str2:	.asciiz	“Sum = ”

.text

main:

li $s0, 0		# sum = 0

loop:

li	$v0, 4		# Print string

la	$a0, str

syscall

li	$v0, 5		# Take input

syscall

beq $v0, $0, done	# if zero was input, end and display sum

add $s0, $s0, $v0	# sum = sum + input

j	loop		# jump to input another number

done:

li	$v0, 4		# Print string

la	$a0, str2

syscall

li	$v0, 1		# Print sum

move	$a0, $s0

syscall

.end

- sll    $t0, $t3, 9		# Shift bits to most significant position

srl    $t0, $t0, 15		# Shift back to least significant, shifting in 0’s

4.

addi	$v0, $zero, 0		# Initialize count

Loop:

lw	$v1, 0($a0)		# Read next word from source

sw	$v1, 0($a1)		# Write to destination

addi	$a0, $a0, 4 		# Advance pointer to next source

addi	$a1, $a1, 4  		# Advance pointer to next destination

beq	$v1, $zero, done	# Done if word copied = zero

addi	$v0, $v0, 1		# Increment counter

j	Loop			# Loop to copy next word

Done:					# Done coping words, continue on

- The assembler might have trouble directly implementing the code because it can only skip a limited number of instructions with the branch.  Using PC relative addressing, the branch can go to any instruction between PC+2^16-1 and

PC-2^16+1.  If the distance between “here” and “there” is greater than that, it cannot directly implement the branch.  A possible reworking is:

Here: 		bne       $s0, $s2, next

j there

Next:

….

There		add	$s0, $s0, $s0

Now the branch must only skip one instruction, and the jump will take care of moving to “there”.