Assignment 11 Solutions

- In MIPS:

SumArray:

addi $v0, $zero, 0

addi $t0, $zero, 0

Loop:

beq $t0, $a1, Endloop

lw $t1, 0($a0)

addi $a0, $a0, 4

add $v0, $v0, $t1

addi $t0, $t0, 1

j Loop

Endloop:

jr $ra

In PPC:

SumArray:

addi $r5, $zero, 0

addi $r6, $zero, 0

Loop:

cmpw $r6, r4

beq Endloop

lw $r7, 0($r3)

addi $r3, $r3, 4

add $r5, $r5, $r7

addi $r6, $r6, 1

b Loop

Endloop:

mr $r5, $r3

blr

b) MIPS: 6N + 3

PPC: 7N + 4

c) MIPS 9*4 = 36 Bytes

PPC: 11*4 = 44 Bytes

- Bob should use the complements of Q0-Q2 and ignore Q3.  This will give him a 3 bit down counter.

i) 5x5

| Iteration | Multiplicand | Step | F | Product |
| --- | --- | --- | --- | --- |
| 0 | 0101 | Initial Values | 0 | 0000 | 0101 |
| 1 | 0101 | 1: prod = prod + mcand | 0 | 0101 | 0101 |
|  | 0101 | shift right | 0 | 0010 | 1010 |
| 2 | 0101 | 0: no operation | 0 | 0010 | 1010 |
|  | 0101 | shift right | 0 | 0001 | 0101 |
| 3 | 0101 | 1: prod = prod + mcand | 0 | 0110 | 0101 |
|  | 0101 | shift right | 0 | 0011 | 0010 |
| 4 | 0101 | 0: no operation | 0 | 0011 | 0010 |
|  | 0101 | Arith shift right | 0 | 0001 | 1001 |

ii) 5x-5

| Iteration | Multiplicand | Step | F | Product |
| --- | --- | --- | --- | --- |
| 0 | 0101 | Initial Values | 0 | 0000 | 1011 |
| 1 | 0101 | 1: prod = prod + mcand | 0 | 0101 | 1011 |
|  | 0101 | shift right | 0 | 0010 | 1101 |
| 2 | 0101 | 1: prod = prod + mcand | 0 | 0111 | 1101 |
|  | 0101 | shift right | 0 | 0011 | 1110 |
| 3 | 0101 | 0: no operation | 0 | 0011 | 1110 |
|  | 0101 | shift right | 0 | 0001 | 1111 |
| 4 | 0101 | 1: prod = prod - mcand | 0 | 1100 | 1111 |
|  | 0101 | Arith shift right | 0 | 1110 | 0111 |

iii) -5x5

| Iteration | Multiplicand | Step | F | Product |
| --- | --- | --- | --- | --- |
| 0 | 1011 | Initial Values | 0 | 0000 | 0101 |
| 1 | 1011 | 1: prod = prod + mcand | 1 | 1011 | 0101 |
|  | 1011 | shift right | 1 | 1101 | 1010 |
| 2 | 1011 | 0: no operation | 1 | 1101 | 1010 |
|  | 1011 | shift right | 1 | 1110 | 1101 |
| 3 | 1011 | 1: prod = prod + mcand | 1 | 1001 | 1101 |
|  | 1011 | shift right | 1 | 1100 | 1110 |
| 4 | 1011 | 0: no operation | 1 | 1100 | 1110 |
|  | 1011 | Arith shift right | 1 | 1110 | 0111 |

iv)-5x-5

| Iteration | Multiplicand | Step | F | Product |
| --- | --- | --- | --- | --- |
| 0 | 1011 | Initial Values | 0 | 0000 | 1011 |
| 1 | 1011 | 1: prod = prod + mcand | 1 | 1011 | 1011 |
|  | 1011 | shift right | 1 | 1101 | 1101 |
| 2 | 1011 | 1: prod = prod + mcand | 1 | 1000 | 1101 |
|  | 1011 | shift right | 1 | 1100 | 0110 |
| 3 | 1011 | 0: no operation | 1 | 1100 | 0110 |
|  | 1011 | shift right | 1 | 1110 | 0011 |
| 4 | 1011 | 1: prod = prod - mcand | 1 | 0011 | 0011 |
|  | 1011 | Arith shift right | 1 | 0001 | 1001 |

- a)

- Canonical sop:

X_new = X’Y’I’ + X’YI + XY’I + XYI’

Y_new = X’Y’I’ + X’Y’I + XY’I’ + XY’I

Simplified sop:

X_new = I (X xor Y) + I’ (X xnor Y)

Y_new = Y’

- i) 00  ii) 10 iii) 01

- a)

b)

| Current State | Next State | Output |
| --- | --- | --- |
| x2 | x1 | x0 | y2 | y1 | y0 | Out2 | Out1 | Out0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 |
| 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 |
| 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 |
| 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 |
| 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 |
| 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 |
| 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 |
| 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 |

c)    Canonical SoP

y2 = x2’x1x0 + x2x1’x0’ + x2x1’x0 + x2x1x0’

y1 = x2’x1’x0 + x2’x1x0’ + x2x1’x0 + x2x1x0’

y0 = x2’x1’x0’ + x2’x1x0’ + x2x1’x0’ + x2x1x0’

Out2 = x2’x1’x0’ + x2’x1’x0 + x2’x1x0’ + x2’x1x0

Out1 = x2’x1x0’ + x2’x1x0 + x2x1x0’ + x2x1x0

Out0 = x2’x1’x0 + x2’x1x0’ + x2’x1x0 + x2x1’x0 + x2x1x0’ + x2x1x0

Simplified version:

y2 = x2’x1x0 + x2x0’ + x2x1’

y1 = x1 xor x0

y0 = x0’

Out2 = x2’

Out1 = x1

Out0 = x1 + x0

d)

| Current State | Input | Next State |
| --- | --- | --- |
| x2 | x1 | x0 | I | y2 | y1 | y0 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 1 | 0 | 0 | 1 |
| 0 | 0 | 1 | 0 | 0 | 1 | 0 |
| 0 | 0 | 1 | 1 | 1 | 0 | 0 |
| 0 | 1 | 0 | 0 | 0 | 1 | 1 |
| 0 | 1 | 0 | 1 | 0 | 1 | 1 |
| 0 | 1 | 1 | 0 | 0 | 0 | 0 |
| 0 | 1 | 1 | 1 | 1 | 0 | 0 |
| 1 | 0 | 0 | 0 | 0 | 0 | 0 |
| 1 | 0 | 0 | 1 | 0 | 0 | 0 |

# Text boxes

1

11

10

01

00

0

0

1

0

1

0

1

0

100

1

100

000

101

001

010

111

a)

110

011

100

0

111

011

011

111

001

101

000

100

011

1

010

1

001

0

000

1

0

1

0

1

0,1

2

0

4

1

0

3

1

0

1

5

1

b)

0

1

1

2

1

1

3

1

0,1

4

0

0

0

0