Assignment 6 Solutions

- f1 can be simplified to f1 = x1'.x2' + x1'.x3' + x1.x2.x3

f2 can be simplified to f2 = x1'.x2' + x2'.x3' + x1.x2.x3

So the PLA looks like:

- Problem 3.2:

Truth table for circuit in 3.1

| x1 | x2 | x3 | f |
| --- | --- | --- | --- |
| 0 | 0 | 0 | 0 |
| 0 | 0 | 1 | 1 |
| 0 | 1 | 0 | 1 |
| 0 | 1 | 1 | 0 |
| 1 | 0 | 0 | 1 |
| 1 | 0 | 1 | 0 |
| 1 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 |

In the circuit in 3.2, if x1 = x2 = 0 (the top two rows of the truth table) or if x1 = x2 = 1 (the bottom two rows of the truth table) f = x3.  When x1 does not equal x2 (the middle four rows) f = x3’.  So the circuit produces an equivalent truth table.

The circuit requires 1 not gate and 3 2-1 multiplexers.  Using transmission gates to implement the multiplexers, each one takes 6 transistors.  Thus, the total number of gates required in the circuit is 20.

- Problem 3.3

Truth table for 3.3

| x1 | x2 | x1^x2 | x3 | f = x3^x1^x2 |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 |
| 0 | 0 | 0 | 1 | 1 |
| 0 | 1 | 1 | 0 | 1 |
| 0 | 1 | 1 | 1 | 0 |
| 1 | 0 | 1 | 0 | 1 |
| 1 | 0 | 1 | 1 | 0 |
| 1 | 1 | 0 | 0 | 0 |
| 1 | 1 | 0 | 1 | 1 |

The truth table is equivalent to that in 3.1 and 3.2.

Each xor gate takes 8 transistors if implemented as in figure 3.61d.  Thus, for the 2 xor gates, the total number of transistors required is 16.

- Problem 3.49

a)  f = x1x2 + x3,  One of the many possible solutions is:

b) f = x1x3 + x2x3, One of the many possible solutions is:

- Problem 4.12

Karnaugh map for f			Karnaugh map for g

x1x2

| x3x4 | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 1 | 1 |  |  |
| 01 |  |  |  | 1 |
| 11 |  | 1 |  | d |
| 10 | 1 | 1 |  | d |

x1x2

| x3x4 | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | d | 1 |  |  |
| 01 |  |  | d | 1 |
| 11 |  |  | 1 |  |
| 10 | 1 |  | d | 1 |

f = x1’x4’ + x1’x2x3 + x1x2’x4

g = x1’x3’x4’ + x1x3’x4 + x1x2x4 + x2’x3x4’

Total cost to implement f alone is 4 gates plus 11 inputs, or 15.

Total cost to implement g alone is 5 gates plus 16 inputs, or 21.

So to implement both separately, the cost is 15+21 = 36.

Implementing f and g together:

f = x1’x3’x4’ + x2’x3x4’+ x1’x2x3 + x1x2’x3’x4

g = x1’x3’x4’ + x2’x3x4’ + x1x2x4 +  x1x2’x3’x4

Terms in bold are reusable.  So there are 7 gates required with a total of 24 inputs, making the new total cost 7 + 24 = 31.

- Problem 4.32

| X1 | X2 | X3 | X4 | X5 | f | g |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 1 | 1 |
| 0 | 0 | 0 | 0 | 1 | 0 | 0 |
| 0 | 0 | 0 | 1 | 0 | 1 | 1 |
| 0 | 0 | 0 | 1 | 1 | 0 | 0 |
| 0 | 0 | 1 | 0 | 0 | 1 | 1 |
| 0 | 0 | 1 | 0 | 1 | 1 | 1 |
| 0 | 0 | 1 | 1 | 0 | 0 | 0 |
| 0 | 0 | 1 | 1 | 1 | 0 | 0 |
| 0 | 1 | 0 | 0 | 0 | 0 | 0 |
| 0 | 1 | 0 | 0 | 1 | 0 | 0 |
| 0 | 1 | 0 | 1 | 0 | 0 | 0 |
| 0 | 1 | 0 | 1 | 1 | 0 | 0 |
| 0 | 1 | 1 | 0 | 0 | 0 | 0 |
| 0 | 1 | 1 | 0 | 1 | 0 | 0 |
| 0 | 1 | 1 | 1 | 0 | 0 | 0 |
| 0 | 1 | 1 | 1 | 1 | 0 | 0 |
| 1 | 0 | 0 | 0 | 0 | 1 | 1 |
| 1 | 0 | 0 | 0 | 1 | 0 | 0 |
| 1 | 0 | 0 | 1 | 0 | 1 | 1 |
| 1 | 0 | 0 | 1 | 1 | 0 | 0 |
| 1 | 0 | 1 | 0 | 0 | 1 | 1 |
| 1 | 0 | 1 | 0 | 1 | 1 | 1 |
| 1 | 0 | 1 | 1 | 0 | 1 | 1 |
| 1 | 0 | 1 | 1 | 1 | 1 | 1 |
| 1 | 1 | 0 | 0 | 0 | 0 | 0 |
| 1 | 1 | 0 | 0 | 1 | 0 | 0 |
| 1 | 1 | 0 | 1 | 0 | 0 | 0 |
| 1 | 1 | 0 | 1 | 1 | 1 | 1 |
| 1 | 1 | 1 | 0 | 0 | 0 | 0 |
| 1 | 1 | 1 | 0 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 | 0 | 1 | 1 |
| 1 | 1 | 1 | 1 | 1 | 1 | 1 |

Functions are equivalent.

- Problem 6.16

One possible solution is:

i1 = w2, i2 = w2, i3 = w1, i4 = w3, i5 = w3, i6 = w1, i7 = w3’, i8 = 1.

- Worst case delay = t_fulladder + t_2-1-mux + t_4-1-mux + t_gate.

- Add worst case delay = t_fulladder + t_2-1-mux + t_4-1-mux

Sub worst case delay = t_fulladder + t_2-1-mux + t_4-1-mux + t_gate

And worst case delay = t_gate + t_4-1-mux

Or worst case delay = t_gate + t_4-1-mux

Other worst case delay = t_4-1-mux

- Worst case for 4 bit alu is subtraction:

t_gate (for not b) + t_2-1-mux + t_CLA + 2*t_gate (for add operation) + t_4-1-mux

Total = 3* t_gate + t_2-1-mux + t_CLA + t_4-1-mux