# CPR E 381x/382x ( Labw02a and Labw02b

# Single Cycle CPU Implementation

1. Objectives

In this lab you will implement a single-cycle MIPS instruction subset.

2. Prelab

Understand the single-cycle datapath, control unit and ALU control.

3. Setup

As you did in previous labs, make sure you create the folder in your home directory U:\CPRE381\Labw02a, and then a sub-folder ~\cpu.

4. CPU in Verilog

Figure 5.24 in your Patterson & Hennessy textbook shows the single cycle datapath with control units. Instead of implementing a 32-bit wide datapath processor, you are required to create a 16-bit single cycle CPU. Modify the datapath accordingly to accommodate the 16-bit wide requirement. IMPLEMENT THE CONTROL BLOCK

Instruction Format

| J Format | OPCODE | ADDRESS |
| --- | --- | --- |
|  | 15:12 | 11:0 |

| I/LW/SW/BEQ/BNE Format | OPCODE | IMM/OFFSET | RT | RS |
| --- | --- | --- | --- | --- |
|  | 15:12 | 11:8 | 7:4 | 3:0 |

| R Format | OPCODE | RD or SHIFT | RT | RS |
| --- | --- | --- | --- | --- |
|  | 15:12 | 11:8 | 7:4 | 3:0 |

OPCODES

| Opcode | Instruction Operation |
| --- | --- |
| 0000 | add |
| 0001 | and |
| 0010 | or |
| 0011 | slt |
| 0100 | lw |
| 0101 | sw |
| 0110 | beq |
| 0111 | bne |
| 1000 | addi |
| 1001 | andi |
| 1010 | ori |
| 1011 | slti |
| 1100 | sub |
| 1101 | shift |
| 1110 | jr |
| 1111 | jal |

Verify with TA of your design.

CPR E 381x/382x ( Labw02a and Labw02b   Answer Sheet

# Single Cycle CPU Implementation

Name____________________

Name____________________

- Single Cycle CPU

TA Initials: __________