# CPR E 381x/382x ( Labw05a

# Forwarding and Hazard Detection Unit Design

1. Objectives

The purpose of this lab is to design forwarding and hazard detection unit so that you can put these two units into the pipelined cpu design next lab.

2. Prelab

Read the relevant sections of your textbook about data hazards and forwarding and understand how the two units work in the pipelined processor.

3. Setup

As usual, create the folder in your home directory U:\CPRE381\Labw05a, and then two sub-folders ~\hazard, ~\forward.

The forward unit with required multiplexers selects register input to ALU in ALU stage. The hazard detection unit inserts a NOP instruction between a load word instruction and a subsequent instruction that needs to read the register being loaded.

4. Forwarding Unit

Design a forwarding unit as follows (note that it consists of only combinatorial logic):

FORWARD (IDEXRA1, IDEXRA2, EXMEMWA, MEMWBWA, EXMEMWRF, MEMWBWRF, IDEXRD1, IDEXRD2, EXMEMWD, MEMWBWD, ALUIND1, ALUIND2).

| Variable | Meaning |
| --- | --- |
| IDEXRA1, IDEXRA2 | 4-bit addresses of registers just read from register file |
| IDEXRD1, EDEXRD2 | 16-bit values that are the contents of the registers read |
| EXMEMWA, MEMWBWA | 4-bit addresses of the registers that could be written by the instructions in those stages |
| EXMEMWD, MEMWBWD | Corresponding (the last row) 16-bit data values |
| EXMEMWRF, MEMWBWRF | Values of the signals indicating if the instructions in those stages will be writing into the register file |
| ALUIND1, ALUIND2 | Values ALU stage must use for actual computation |

5. Hazard Detection

Design a hazard detection module as follows:

HAZARD (IDEXMR, IDEXWA, IFIDRA1, IFIDRA2, IFIDWE, INHINC, NOP)

| IDEXMR | 1-bit indicator if instruction in ID/EX is a memory read |
| --- | --- |
| IDEXWA | 4-bit register address the ID/EX inst is writing |
| IFIDRA1, IFIDRA2 | Two 4-bit register addresses being read in ID stage |
| IFIDWE | 1-bit value enabling writing to the IF/ID register by IF |
| INHINC | 1-bit signal inhibiting the incrementing of the PC |
| NOP | 1-bit MUX control choosing the control bits into the ID/EX reg |

Show your TA the code for your FORWARD and HAZARD modules and their tests.

CPR E 381x/382x ( Labw05a Answer Sheet

# Forwarding and Hazard Detection Unit

Name____________________

Name____________________

- Forwarding

TA Initials: ____________

- Hazard Detection

TA initials: ____________