# CPR E 381x/382x ( Labw05b, Lab06a

# Pipelined CPU Implementation

1. Objectives

In this lab you will implement a pipelined MIPS like processor.

2. Prelab

Understand the pipelined datapath, control unit, forwarding, and hazard detection unit.

3. Setup

As you did in previous labs, make sure you create the folder in your home directory U:\CPRE381\Labw05b, and then a sub-folder ~\cpu.

4. CPU in Verilog

Figure 6.36 in your Patterson & Hennessy textbook shows the pipelined datapath with control, forwarding, hazard detection units. As you did in previous labs, instead of implementing a 32-bit wide datapath processor, you are required to create a 16-bit wide CPU. Modify the datapath accordingly to accommodate the 16-bit wide requirement and our chosen instruction set.

Instruction Format

| J Format | OPCODE | ADDRESS |
| --- | --- | --- |
|  | 15:12 | 11:0 |

| I/LW/SW/BEQ/BNE Format | OPCODE | IMM/OFFSET | RT | RS |
| --- | --- | --- | --- | --- |
|  | 15:12 | 11:8 | 7:4 | 3:0 |

| R Format | OPCODE | RD or SHIFT | RT | RS |
| --- | --- | --- | --- | --- |
|  | 15:12 | 11:8 | 7:4 | 3:0 |

OPCODES

| Opcode | Instruction Operation |
| --- | --- |
| 0000 | add |
| 0001 | and |
| 0010 | or |
| 0011 | slt |
| 0100 | lw |
| 0101 | sw |
| 0110 | beq |
| 0111 | bne |
| 1000 | addi |
| 1001 | andi |
| 1010 | ori |
| 1011 | slti |
| 1100 | sub |
| 1101 | shift |
| 1110 | jr |
| 1111 | jal |

The following is a sequence of instructions you need to use to test your design:

0	addi	 r1, r0, 7		//r1=7

2	andi	 r5, r0, 3		//r5=0

4 	add	 r6, r1, r1		//r6 = 14

6	addi  r6, r6, 6		//r6 = 20

loop1:

8	sw	 r1, 7(r5)		//Mem[7]=7, 3, -1

10	lw	 r2, 7(r5)		//r2=Mem[7] = 7, 3, -1

12	and	 r4, r2, r5		//r4=0, 0, 0

14	or	 r8, r2, r6		//r8=23, 23, -1

16	add	 r9, r6, r2		//r9= 27, 23, 19

18	slt	 r7, r6, r9		//r7=1, 1, 0

20	bne	 r7, r0, 6       //Jump to PC + 6 (instruction 34)

22	shift right, r9, r9		//r9>>1, r9=9

24	addi	 r2, r0, 7		//r2=7

26	sub	 r9, r9, r2		//r9=2, -5

28	slti	 r14, r9, 2		//r14=0, 1

30	beq	 r14, r0, -3     //Jump to PC – 3 (Instruction 26)

32	jr	 r15			//Should jump to 38

34	addi	 r1, r1, -4		//r1=3, -1

36	jal	 loop1			//r15=38

38	add	 r0, r0, r0		//no-op

Verify with TA of your design.

CPR E 381x/382x ( Labw05b

Answer Sheet

# Pipelined CPU Implementation

Name____________________

Name____________________

- Pipelined CPU

TA Initials: ____________

DATE: _____________