## Slide 1: Practical Energy-aware Real-Time Systems
2012.10.24
2013.09.23 (updated)
Koo

## Slide 2: Warm-up Question
What the most energy consuming case in your wireless device? (off-line & on-line)
My answer:
When you use your smart phone for HD video recoding, you will use maximum capacity of application processor, camera, LCD, microphobne, etc.
When you use your smart phone for video call in poor antenna condition, you will use maximum capacity of communication/application processor, camera, LCD, microphone, speaker, etc.
When you use your smart phone for video call in poor antenna condition on your fast moving, it will be one of the most power consuming case.

## Slide 3: Energy-aware Real-Time Systems
There will be three main types of power management techniques.
DVFS (Dynamic Voltage & Frequency Scaling)
DMS (Dynamic Modulation Scaling)
Network Coding

## Slide 4: Energy-aware Real-Time Systems
Contents
Part I. Introduction of Practical Real-Time systems
Part II. Energy-aware Real-time scheduling (DVFS)
Part III. Introduction of Network Coding

## Slide 5: Part I. Introduction of Practical Real-Time systems
Contents
Block diagram
Function applications
Case study by worse case
Power consumption by L-04A (NTT DoCoMo)
Conclusion

## Slide 6: 1. Block Diagram
Application processor
with modem
RF ICs
[LTE, WCDMA, GSM, GPS, etc.]
Memory (DRAM, eMMC)
PMIC
I/O devices

## Slide 7: 1. Block Diagram (RF; e.g. Qualcomm RTR8600)
RF IC
GSM
WCDMA
LTE
GPS
GSM PA
WCDMA dual PA
RX SAW
* PA : Power Amplifier
* SAW : Surface Acoustic Wave
* RX: Receiving
* TX : Transmitting
* SP6T: Single Pole 6 Throws
SP 6T
Coupler
Duplexer
TX SAW
TX SAW
Coupler
Duplexer
There are various types of RF ICs such as Blue Tooth, WLAN, and RFID.

## Slide 8: 1. Block Diagram (Baseband; e.g. Qualcomm MSM8960)
Application processor
with modem
Memory (DRAM, MMC)
PMIC
I/O devices
LCD
Camera
Speaker
Vibrator
USB
Keypad
Battery
Adapter
LPDDR2 SDRAM
eMMC
*LPDDR : Low Power Double Data Rate
* eMMC : embedded Multi Media Card

## Slide 9: 2. Function application (LCD operation)
MSM 8960
MDP (Mobile Display Processor)
HDMI
(High Definition
Multimedia Interface)
MIPI
(Mobile Industry
Processor Interface)
LCD
Camera
LED backlight
 When a LCD module operates, it needs a LED backlight. A LCD module displays an image by LED backlighting. The backlight is one of major power consumptions in a cell phone . Its amount depend on brightness of LCD.
PMIC

## Slide 10: 2. Function application (wireless communication)
Wireless communications
Bluetooth
GSM, WCDMA, HSPA, LTE
GPS
RFID
IrDA (Infrared Data Association)
Wireless LAN
Modes of
power amplifier
Stand-by mode
Low mode
Middle mode
High mode
Max. power owing to lack of connectivity

## Slide 11: Example(from previous slide)
A brief flow chart of power scheduling
Computation System(off-line operation)
Idle mode
Sleep mode
Active mode
Communication System (on-line operation)
Medium power
mode
High power
mode
Low power
mode
Communication
off / on
Power-on
Start-up
Low freq. & low vtg.
High freq. & low vtg.
*For DVS, there are low & high frequency clocks . DC converter and LDO provide various types of voltages.
High freq. & high vtg.
*Low /medium/high power mode is decided by antenna condition.
Three types of call modes

## Slide 12: 3. Case study (worse case)
Video call & high power mode on WCDMA
: This case needs a LCD and a camera with the max. power of power amplifier at WCDMA communication.
RFIC
Application processor
with modem
Memory (DRAM, MMC)
PMICs
WCDMA
WCDMA dual PA
Coupler
Duplexer
TX SAW
LCD
LED backlight
Camera

## Slide 13: 4. Power consumption by L-04A (NTT DoCoMo)
The most power consumption 5 & 5
No. | Condition1 | Condition 2 | TX power | Current consumption [Vin= 3.8V]
1 | W2100 | VT | 23 dBm | 732mA
2 | W800 | VT | 23 dBm | 721mA
3 | W800 | Talk | 23 dBm | 520mA
4 | W2100 | VT | 12 dBm | 487mA
5 | W800 | VT | 12 dBm | 480mA
No. | Condition1 | Condition 2 | Current consumption [Vin= 3.8V]
1 | Camera | VGA CAMERA | 250mA
2 | Camera | 2M CAMERA | 213mA
3 | MP3 | Speaker | 92mA
4 | MP3 | Ear-mic | 57.5mA
5 | Stand-by |  | 1mA

## Slide 14: 5. Conclusion
Multimedia parts (ARM core, power regulators, LCD, camera, etc.) are the major part of power consumption when a wireless embedded system does not work for communication.
RX power amplifier, RF module will also critical when the system work for wireless communication.

## Slide 15: Part II. Energy-aware Real-time scheduling
Contents
PMIC
System Block Diagram
Case Study (DVFS)
General methods of Power Management
Future Works

## Slide 16: 1. PMIC (Power Management IC)
Why do we need PMIC?
-. From a single battery to various types of inside modules and I/O devices, PMIC controls their power.
What are its main tasks?
-. Input power (battery, charger, USB)
-. Output power (SMPS, LDO, charge pump) ; DVFS
-. IC interface (PA control, GPIO)
-. General housekeeping by internal CLKs
-. User Interface (LED, LCD, Vibrator, Headset, Speaker)

## Slide 17: 2. System Block Diagram
RF(Radio Frequency) vs. BB (Baseband)
Application processor
with modem
RF ICs
[LTE, WCDMA, GSM, GPS, etc.]
Memory (DRAM, MMC)
PMIC
I/O devices

## Slide 18: 3. DVFS (Dynamic Voltage and Frequency Scaling)
DVFS
-. According to scheduled modes, PMIC provides processors’ core with different types of power by scaling voltage and frequency.

## Slide 19: 4. General Power Management
Step 1) Analyze a target task/application
: min./max. power requirement
Step 2) Seek leakage/unnecessary power
e.g.) pending task after interrupt
Step 3) Make up a specific algorithm with possible scenarios
e.g.) DVFS, FSM, etc.
Step 4) Verify a side effect after testing a new PM algorithm

## Slide 20: Part III. Introduction of Network Coding
Contents
Basic concept of Network Coding
Why Network Coding is beneficial?
My algorithm to select the best TX one(s)
Testbed for Network-coding algorithm

## Slide 21: 1. Basic concept of Network Coding
When a relay needs to send several messages to clients, the relay will use their resource by XOR.
Bob
Alice
A
B
Relay
A
Alice’s packet
B
Bob’s packet
B
Bob’s packet
A
Alice’s packet
B
A
XOR
=

## Slide 22: 1. Basic concept of Network Coding
If the relay does not use clients’ resource, it will need one more transmission.
Bob
Alice
A
Relay
A
Alice’s packet
B
Bob’s packet
B
Bob’s packet
A
Alice’s packet
A
B
B

## Slide 23: 2. Why Network Coding is beneficial?
Alice
Relay
Bob
Charlie
A
Alice’s packet
A
Alice’s packet
A
Alice’s packet
C
Charlie’s packet
B
Bob’s packet
B
Bob’s packet
B
Bob’s packet
C
Charlie’s packet
C
Charlie’s packet
Alice Bob
Bob Charlie
Charlie Alice
A
B
C
C
A
B
XOR
=
XOR

## Slide 24: 2. Why Network Coding is beneficial?
When the relay transmits a Network-coded message, it will take one transmission energy rather than multiple transmission energy. (Multicasting Network duplicates the coded message)
Relay
Range of Wireless Network
Multicasting Network
TX
Alice
Bob
Charlie
RX
RX
RX

## Slide 25: 3. My algorithm to select the best TX one(s)
Given conditions
R
C1
C2
C3
I need {A}.
I have {B, C}.
I need {B}.
I have {C, A}.
I need {C}.
I have {A}.
I will transmit {A, B, C}. Then how?

## Slide 26: 3. My algorithm to select the best TX one(s)
Given conditions
Matrix for Required Messages =
Matrix for Resource in clients =
Then assemble them together.

A B C
A B C
A B C

## Slide 27: 3. My algorithm to select the best TX one(s)
Steps of my algorithm
Step 1)  Look for whether there is ‘1’ in the column.
Step 2)
If there are n ‘1’s, check whether there are (n-1) columns which has n ‘1’s. If no pair, go to n-1.
Repeat until n =2
Step 2-1)
Step 2-1-2)
Step 2-1-3)
Both step 2-2 or step 2-3 are possible.

## Slide 28: 3. My algorithm to select the best TX one(s)
Steps of my algorithm
Step 2-1-2)
I take step 2-1-2; TX1=A (XOR) B
Step 2-2)
If one candidate is selected, the whole rows will be null. Then go to the next row.
Step 2’)
If there is not ‘1’ , the TX will be itself
; TX2=C
Step 2’-1)
If one candidate is selected, the whole rows will be null. Then go to the next row.

## Slide 29: 3. My algorithm to select the best TX one(s)
Steps of my algorithm
Step 3)
If there is not ‘1’ in the assembled matrix, TX is completed.

## Slide 30: 4. Testbed for Network-coding algorithm
Network Algorithms are tested by Android devices.
Demonstration 1

## Slide 31: 4. Testbed for Network-coding algorithm
Network Algorithms are tested by Android devices.
Demonstration 2
C1
C2
R
1) A
1) B
2) A (XOR )B
3)
B= A (XOR )B (XOR) A
3)
A= A (XOR )B (XOR) B

## Slide 32: 4. Testbed for Network-coding algorithm
Network Algorithms are tested by Android devices.
Demonstration 3
C1
C2
R
1) A
3) B
2) A
4) B

## Slide 33: Q&A
Please give me a question which you are interested in or not clear.
Thank you.

## Slide 34: References
Qinglong Liu, and Gang Feng “Optimization Based Queue Management for Opportunistic Network Coding” , 2011 6th International ICST Conference on Communications and Networking in China ,2011, pp 1159-1164
S. Katti, H. Rahul, W. Hu, D. Katabi, M. M. Medard and J. Crowcroft, “XORs in the Air”: Practical Wireless Network Coding,” in Proc. of ACM SIGCOMM’06, Pisa, Italy, Sept. 2006.
R. Ahlswede, N. Cai, S. Y. R. Li, and R. W. Yeung, “Network Information Flow”, IEEE Transactions on Information Theory, vol. 46, no. 4, July 2000, pp.1204-1216.
P. Glatz, J. Loinig, C. Steger, and R. Weiss, “A first step towards energy management for network coding in wireless sensor networks,” in 9th IEEE Malaysia International Con-ference on Communications, dec. 2009, pp. 905 – 910.