Reconfigurable Computing: Homework 2

(CPRE 583, Fall 2010)

Due: Wed 10/6/2010

- State machines (5 pts)

  - Draw a Mealy and Moore statemachine bubble diagram for each the following patterns. Make sure to detect overlapping patterns.  For example “0110110” contains two “0110” patterns.

    - 1110

    - 0110

- VHDL to FPGA implementation example  (Still being developed) (60 pts)

  - Draw a block/schematic diagram for the VHDL given in HW2.vhd (see course webpage) . (10 pts)

    - For the statemachine portion of the diagram draw the bubble diagram within a box, and show the inputs and outputs to and from the box containing the bubble diagram.

  - Synthesis the design into D flip-flops, inverters, and two input AND and OR gates. (10pts)

  - Map the synthesized design to D flip-flops and 3 input LUTs.  (10 pts)

    - Name each LUT that gets allocated A, B, C, …  And name each D flip-flop allocated DFF_A, DFF_B, …

    - How many LUT and how many D flip-flops did you use.

  - Place the D flip-flops and LUTs on the FPGA given on the PowerPoint slide that can be found on the course webpage. (10 pts)

    - Label each placed LUT and D flip-flop using the names from c.)

    - Highlight each used component in red.

  - Route the design. (10 pts)

    - Highlight all the used routes in red.

  - Configure the FPGA (10 pts)

    - Program all the boxes given in the PowerPoint slide.  Note: since many will be high impendence (e.g. Z), I’ve initially filled most in as Z.

- Looking inside the FPGA (if you are using NX, then make sure to add all the NX font packages or fpga_editor will give a segmentation fault error)  (10 pts)

  - Use fpga_editor to look at the MAPed version of MP1. After starting fpga_editor you will open MP1_top_map.ncd:  Look around the design (7 pts)

    - Identify 4 components. Two should be components that we have talked about little or not at all in class

    - Write 1-2 paragraphs about each of the 4 components (use the Virtex 5 user guide to help find information)

  - Now use fpga_editor to open MP1_top.ncd. This is the post PAR version (3 pts)

    - What is the main difference between MP1_top_map.ncd, and MP1_top.ncd.  Turn on all the display options that the GUI gives to get a feel for the amount of detail that exists within the FPGA.

    - Step into one of the slices in the design (double click).  Write down the equation for one of the LUTs

- Trade-offs on reconfiguration granularity. (10 pts)

  - Give a half to a full page discussion on the trade-offs associated with the size of the granularity used for a reconfiguration fabric.

- Garp Details (15 pts)

  - Read “The Garp Architecture and C compiler” year: 2000.  This can be found on IEEE Xplorer.

  - Reducing reconfiguration time

    - What aspects of the Garp design help mitigate overheads associated with reconfiguration time?

    - Why is having a low reconfiguration time important in general?

  - What implementation aspects of Garp help make multiplying by small constants efficient?

  - Why is the iteration spacing in Figure 3 of the paper two clock cycles?

  - In table 2 why does it make sense that strlen of a 1024 char string is accelerated more than strlen of a 16 character string?