## Slide 1: Nonlinearities for current-steering DACs
Static nonlinearities (dc or low frequencies)
  Random mismatch errors
  Gradient effect
  Finite output impedance
Dynamic nonlinearities (high frequencies)
  Dynamic output impedance
  Finite settling time
  Charge injection
  Switch timing errors
Nonlinearities associated with this architecture limit its potential to achieve higher speed

## Slide 2: State of the art
Speed is not a issue in modern CMOS technology
  Have achieved several hundreds of MHz or even a few GHz in some cases of sampling rate
Linearity lacks for many existing DACs
  Drastically degrade at high signal frequencies
Improving the linearity performance is incredibly challenging, especially for high frequency linearity
Many top research groups have been working on design solutions to improve the poor linearity performance

## Slide 3: A 14-bit intrinsic accuracy Q2 random walk CMOS DAC
Q2 random walk is a famous design technique to compensate the process dependent gradient errors
Q2 (quad quadrant) refers that each MSB current source consists of four (quad) units in every quadrant
“Random walking” the switching sequence of the current sources make the residual gradient errors “randomized”
Quadratic gradient
Residual quadratic gradient
Linear gradient
Apply Q2
No linear gradient
MSB Array

## Slide 4: Contributions and limitations
The first published 14-bit intrinsic accuracy DAC
Great gradient error compensation
Large current source area used to compensate random mismatch error
Poor spurious-free dynamic range (SFDR) performance due to large parasitic capacitance
High frequency linearity lacks
G. Van der Plas, J. Vandenbussche, W. Sansen, M. Steyaert, and G. Gielen, “A 14-bit intrinsic accuracy Q2 random walk CMOS DAC,” IEEE J. Solid-State Circuits, vol 34, pp. 1708−1718, Dec. 1999.

## Slide 5: A self-trimming 14-b 100-MS/s CMOS DAC
The self-trimming technique can effectively compensate the random mismatch error among current sources
A. R. Bugeja, and B. Song, “A self-trimming 14-b 100-MS/s CMOS DAC,” IEEE J. Solid-State Circuits, vol 35, pp. 1841−1852, Dec. 2000.
Self-trimming loop
MSB current source
I
5% - 10% of I

## Slide 6: Track/attenuate output stage
The track/attenuate stage can improve the dynamic linearity by reducing the signal dependence at the output
Isolate the nonlinear transition
Remove previous code dependence

## Slide 7: Contributions and limitations
Great random mismatch error compensation by using self-trimming
Excellent dynamic linearity enhancement by the track/attenuate output stage
One of the best DACs in high frequency linearity performance
Complicated calibration loop (ADC-DSP-DAC)
Less interest in a newer CMOS technology because of the 5-stacked-transistor current source

## Slide 8: A 1.5-V 14-bit 100-MS/s self-calibrated DAC
The self-calibration technique can successfully calibrate the random mismatch errors in the modern low-voltage CMOS technology
Counter controls MSB inputs
j=0, measure LSB current DLSB
j=1-63, measure MSB current
Obtain error by subtracting j DLSB
Store error code in SAR register
Control CALDAC to correct current
Current errors

## Slide 9: Contributions and limitations
Reduce the gate area by a factor of more than 500 compared to the DAC without any calibration
Achieve the smallest area and power of all published 14-bit DACs by far
Significantly improve the settling rate and dynamic linearity due to dramatic parasitic capacitance reduction
Use complicated calibration loop
(ADC-DSP-DAC)

## Slide 10: A 14-bit 200-MHz current-steering DAC with switching-sequence post-adjustment
The SSPA calibration can enhance the matching accuracy by adjusting the switching sequence of current sources after chip fabrication
It uses minimum analog circuits and some digital circuitry instead of the complicated ADC-DSP-DAC loop
T. Chen, and G. Gielen, “A 14-bit 200-MHz current-steering DAC with switching-sequence post-adjustment calibration,” IEEE J. Solid-State Circuits, vol 42, pp. 2386−2394, Nov. 2007.

## Slide 11: Switching strategy for SSPA calibration
Step 1 Sorting
3
4
8
9
10
11
13
2
1
6
5
7
12
15
14
Step 2 Resequencing
3
4
8
9
10
11
13
2
1
6
5
7
12
15
14
Step 3 Summing
3
13
2
1
15
14
4
12
11
5
9
10
6
7
Step 4 Sum Resequencing
Step 5 Final sequencing
9
7
11
5
3
13
10
6
1
15
2
14
4
12
9
7
11
5
3
13
10
6
1
15
2
14
4
12
8
Step 1: sort all current sources
Step 2: Group smaller current with bigger current in neighbor
Step 3: Sum two nearby current sources
Step 4: Group the new smaller current with the new bigger current in neighbor
Step 5: Break up the summed current sources for the final sequencing

## Slide 12: Contributions and limitations
Make the area of current sources only 10% of area required by an intrinsic accuracy DAC
Substantiate the potential of calibrating a DAC with good performance by using only minimum requirement of analog circuits and some digital circuitry
Static performance is not as
good as previous technique
Dynamic linearity deteriorates
at high frequencies

## Slide 13: A 12 bit 2.9 GS/s DAC with IM3 < -60 dBc beyond 1 GHz in 65 nm CMOS
This DAC design extends the 70dB and 60dB SFDR bandwidths to 225MHz and 550 MHz with fsamp > 1GS/s
They recognize the fact that the switching output impedance is a major error source to the DAC’s output distortion
Modified triple-cascode current source is used to improve the dynamic linearity
C.-H. Lin, F.M.I. van der Goes, J. R. Westra, J. Mulder, Y. Lin, E. Arslan, E. Ayranci, X. Liu, and K. Bult, “A 12 bit 2.9 GS/s DAC with IM3 < 60 dBc beyond 1 GHz in 65 nm CMOS,” IEEE J. Solid-State Circuits, vol 44, pp. 3285−3293, Dec. 2009.

## Slide 14: Modified triple-cascode current source
A triple cascode current source is used to enhance the output impedance
Two small current sources are added to keep the switch cascodes always in active, and thus eliminating the switching parasitic capacitance
Switch cascode
Small current source
Small current source (1-2% of I)
Triple cascode (I)

## Slide 15: Contributions and limitations
It has tremendous dynamic linearity enhancement
The first DAC achieves such great SFDR bandwidth extension
The switching capacitance is eliminated; however, the switching resistance still remains
Triple-cascode current source
limits its potential in lower
supply voltage cases

## Slide 16: Complete-folding calibration
Enhance the matching property by dynamically combining the unary current sources into a fully binary-weighted array based on the current comparisons after chip fabrication
Have better performance in compensating random mismatch errors than state-of-the-art

## Slide 17: Switching strategy with 4-bit unary-code array: 1st time folding
Step 1: sort all the current sources in ascending order
Step 2: group the smaller current with the bigger one
Step 3: sum the nearby two currents with one left
Observation:
The first 7 new currents are about the same
They are almost 2-time bigger than the last one
4-bit unary-coded array is turned into 3-bit unary coded and 1-bit binary-weighted array
3
4
8
9
10
11
13
2
1
6
5
7
12
15
14
3
4
8
9
10
11
13
2
1
6
5
7
12
15
14
8
1
15
2
14
3
13
4
12
5
11
6
10
7
9
Use for 2nd time folding
3-bit unary-code and 1-bit binary-weighted array

## Slide 18: Switching strategy with 4-bit unary-code array: 2nd time folding
1
15
2
14
3
13
4
12
5
11
6
10
7
9
7
9
5
11
6
10
2
14
1
15
3
13
4
12
7
9
4
12
5
11
3
13
6
10
1
15
2
14
8
3
2
14
15
10
6
1
5
11
13
4
7
9
12
Step 1 Sort
Step 2 Group
Step 3 Sum
Use for 3rd time folding
2-bit unary-coded and 2-bit binary-weighted array

## Slide 19: Switching strategy with 4-bit unary-code array: 3rd time folding
3
5
11
13
4
7
9
12
15
10
6
1
3
5
11
13
4
7
9
12
15
10
6
1
15
10
6
1
4
7
9
12
3
5
11
13
8
3
4
5
7
9
11
12
13
15
10
6
1
2
14
Step 1 Sort
Step 2 Group
Step 3 Sum
4-bit binary-weighted array

## Slide 20: Comparison of switching sequence
8
3
4
5
7
9
11
12
13
15
10
6
1
2
14
9
7
11
5
3
13
10
6
1
15
2
14
4
12
8
Original sequence
SSPA sequence
Proposed sequence

## Slide 21: General switching strategy
An n-bit unary-coded array can be converted into an (n-1)-bit unary-coded array with 1-bit binary-weighted array by 1-time single-folding
  Example: 1-time single-folding can convert a 4-bit unary-coded array into a 3-bit unary-coded and 1-bit binary-weighted
Complete-folding is to implement (n-1)-time single-folding in an n-bit unary-coded array
  Example: A 4-bit unary-coded array needs 3-time single-folding to ensure complete-folding calibration

## Slide 22: Statistical simulation setup
10,000 14-bit current-steering DAC behavioral models were randomly generated
  7-bit unary-coded MSB array
  7-bit binary-weighted LSB array
Implement 3 calibration techniques separately in the MSB array to compare results
  SSPA Calibration + 20 statistical outlier elimination
  Self Calibration
  Complete-folding Calibration + 20 statistical outlier elimination
The LSB array is realized by intrinsic-accuracy method

## Slide 23: MSB DNL/INL distribution with different calibration techniques