## Slide 1: Chapter 15 - DIB Design

## Slide 2
Purpose of the Device Interface Board
  Definitions:
    DIB: Device Interface Board
    HIB: Handler Interface Board
    PIB: Prober Interface Board
Electrical and mechanical interface between and ATE
  Electrical Interface:
    Distributing the power and signals from the ATE to the DUT
    Signal conditioning to comply with DUT requirements
    Optimizing Tester efficiency by on DIB components
  Mechanical Interface:
    Aligning the DUT from Handler/Prober to DUT contactor on DIB
    Comply with mechanical forces introduced by Handler/Prober when inserting DUT to socket
    Aligning the DIB to the test head of the ATE

## Slide 3
Octal site RF Device Interface Board (DIB)
Hand test socket with DUT
Pogo Interface to ATE resources
Pogo Interface to ATE resources
Components for signal distribution and conditioning

## Slide 4
Recap of ATE, Prober, Handler, HIB and PIB
Different styles of packages require adequate sockets or test/probe contacts

## Slide 5
ATE
DUT output
Relay (open)
1kW load
Leakage test setup
ATE
DUT output
Relay (closed by test program)
1kW load
Distortion test setup
Electromechanical relays modify the DUT’s electrical environment

## Slide 6
DIB Basics
  Purpose of the Device Interface Board
      DUTs that are purely digital in nature typically require a very simple DIB that simply provides point-to-point connectivity between the DUT pins and the tester’s power supplies and digital pin card electronics.
      Analog and mixed-signal DUTs usually require much more elaborate DIBs.
        In fact, DIB design is a fairly major part of mixed-signal test development.
      A mixed-signal DIB will often contain a variety of active and passive circuits that must be connected to (or disconnected from) various DUT pins as the test program progresses.

## Slide 7
Tester instruments
Test head
DIB
Connector block
Tester instruments
Test head
Connector blocks
Socket adapter (mother board)
Swap block (daughter board)
DUT and DUT socket
DUT and DUT socket
Tester instruments
Test head
DIB
Connector block
DUT and DUT socket
Configuration board
(a)
(b)
(b)
(c)
DIB interface schemes
Simple DIB
Socket adapter/swap block
Separate DIB and configuration board

## Slide 8
DIB Basics
  Importance of good DIB Design
      One of the major causes of long test program development time is poor mixed-signal DIB design and printed circuit board design and layout.
      A DIB schematic shows only an idealized view of the DIB. Resistors are shown as ideal resistances, capacitors as ideal capacitances, and traces as perfect connections with no parasitic inductance or capacitance.
      In reality, the exact mechanical layout of the components and traces on the DIB may make the difference between failing test results and passing results.

## Slide 9
DIB Basics
  Importance of good DIB Design
      The performance of analog and mixed-signal devices is highly dependent on the quality of the surrounding circuit design.
        It is important to be able to distinguish between legitimate DUT failures and failures caused by poor design of the DIB.
      Unfortunately, it is difficult to provide the DUT with a perfect environment using a general-purpose tester with bulky electromechanical interconnections.
        For example, the pins of the DUT socket will typically add more inductance and capacitance with an increased cross coupling to the DUT’s environment than it will see when it is soldered directly onto a printed circuit board in the final application.
      Nevertheless, the test engineer has to try to design a DIB that does not present the DUT with electrical handicaps.

## Slide 10
Printed Circuit Boards (PCBs)
  PCB CAD Tools
      Using a netlist-compatible schematic capture tool, the test engineer draws the circuit schematic on a computer workstation or PC using the seed job for the DIB he decided to use.
      Then the schematic database is transferred to the PCB designer for use in the DIB layout process. The layout (footprints) of the components are in the layout level of the design tool
      Once the netlist has been extracted from the database, the PCB designer begins laying out the DIB from a standard DIB template.
      The DIB seedjob represents a head-start DIB design, which includes the shape of the DIB and its standard mechanical mounting holes as well as many pre-placed standard components, such as tester connectors and pogo pads and keep out areas.

## Slide 11
Printed Circuit Boards (PCBs)
  PCB CAD Tools
      The netlist directs the PCB layout software to import all the required DIB components from a standard parts library. The PCB designer then places these components and connects them as shown in the schematic.
      The netlist prevents errors in point-to-point connections by refusing to let the layout designer place traces where they do not belong. The netlist also guarantees that none of the desired connections are mistakenly omitted.
      Once the DIB layout is completed, each layer of the design is plotted onto transparent film for use in PCB fabrication.
      These plots are commonly known as Gerbers, or Gerber plots, named after the company that pioneered some of the early plotting equipment (Gerber Scientific)

## Slide 12
Schematic
Capture
Netlist and BOM
Extraction
DIB
Layout
Starting
with
DIB
Template
Component
Library
Gerber
Plots
PCB
Fabrication
PCB
Assembly and test
Components order

## Slide 13
Printed Circuit Boards (PCBs)
  Multilayer PCBs
    Low-cost PCBs can be designed and fabricated using one or two layers of copper trace.
    Traces on opposite sides of a double-layer PCB can be connected using a copper plated through-hole called a via.
    Double-layer PCB fabrication starts with a blank PCB consisting of a sheet of insulator (e.g. fiberglass) plated on both sides with a thin layer of copper.
    The component lead holes and vias are drilled first.
    Then the holes are plated with copper to form the layer-to-layer interconnects.
    Finally, the traces are printed and etched using a photolithographic process similar to that used in IC fabrication

## Slide 14
Printed Circuit Boards (PCBs)
  Multilayer PCBs
PCB Insulator
(e.g. Fiberglass)
Copper Traces
Single-Layer PCB
Double-Layer PCB
Non-Plated
Through-Hole
Via,
copper-plated through-hole

## Slide 15
Printed Circuit Boards (PCBs)
  Multilayer PCBs
    Multilayer PCBs having four or more layers can be formed by stacking multiple two-layer boards together. The internal, or buried, layers are first printed and etched. Then the layers are all stacked and pressed together under heat to form a single board. Finally, the vias are drilled and plated and the outer layers are etched to form the finished PCB.
+5V Trace
Layer 1 (Signals)
Layer-to-Layer
Signal Interconnect
Layer 2 (Ground Plane)
Layer 3 (+5V Plane)
Layer 4 (Signals)
Grounded Trace

## Slide 16
Printed Circuit Boards (PCBs)
  Multilayer PCBs
    Most mixed-signal DIBs are formed using 6- to 30-layer PCBs. The arrangement of layers in a PCB is known as the stackup.
    The stackup of a DIB may vary from one type of DUT to another, but there are some general guidelines that are commonly followed.
    The internal layers are typically used for ground and power distribution
    Internal layer can be used to shield critical traces between two ground planes (layer).
    The outer layers are usually reserved for critical signals or those signal traces that might need to be modified after the DIB has been fabricated.

## Slide 17
Printed Circuit Boards (PCBs)
  Multilayer PCBs
    In addition to the trace layers and insulator layers in a PCB, the outer layers are usually coated with a material called a solder mask. This thin non-conductive layer keeps solder from flowing all over the traces when the DIB components are soldered onto the PCB. The soldermask helps to prevent unwanted solder shorts between adjacent traces.
    A silkscreened pattern may also be printed on the outer layers of the PCB. The silkscreened patterns show the outline and reference numbers for all the DIB components, such as resistors, capacitors, relays, and connectors and the DUTs. The silkscreened patterns are quite useful during the DIB component assembly process and they are equally useful during the test program debugging process.

## Slide 18
Printed Circuit Boards (PCBs)
  PCB Materials
    Printed circuit boards can be constructed using a variety of materials.
    The most common trace material is copper, due to its excellent electrical conductivity.
    The most common insulator material is FR4 (fire retardant, type 4) fiberglass. Fiberglass is an inexpensive material that exhibits good electrical properties up to several hundred megahertz. As frequencies approach 1 GHz, more exotic materials such as Teflon or cynate ester may be used.

## Slide 19
Printed Circuit Boards (PCBs)
  PCB Materials
    Teflon* exhibits excellent microwave characteristics, including low signal loss and a low dielectric constant. However, it suffers from poor mechanical stiffness.
    Cynate ester is a material with reasonably good high frequency properties and yet it is stiff enough to withstand the mechanical stress of production testing.
    One possible compromise between the good electrical properties of Teflon and the good mechanical properties of cynate ester is a hybrid stackup consisting of sandwiched layers of Teflon and either FR4 or cynate ester

## Slide 20
DIB Traces, Shields and Ground
  Trace Parasitics
    One of the most important DIB components is the printed circuit board (PCB) trace.
    It is easy to think that wires and traces are not components at all, but are instead represented by the connecting lines that appear in a schematic. However, PCB traces are slightly resistive, slightly inductive, and slightly capacitive in nature.
    Often, trace parasitics can be ignored, especially when working with low frequencies and low to moderate current levels. Other times, the parasitics will have a significant effect on a circuit’s behavior. The test engineer should always be aware of the potential problems that trace parasitics might pose.

## Slide 21
DIB Traces, Shields and Ground
  Trace Parasitics
    Trace resistance on DIBs seldom exceeds a few Ohms.
    Inductance can be anywhere from one or two nanohenrys to several microhenrys.
    Capacitance can range from one or two picofarads to tens of picofarads.
    Although these values are very approximate, they can be used as a thumbnail estimate to determine whether the parasitic elements might be large enough to affect the DUT’s performance.
    To estimate trace parasitics with a little more accuracy, we need to review the equations for trace resistance, inductance, and capacitance.

## Slide 22
DIB Traces, Shields and Ground
  Trace Resistance
    The parasitic resistance of a PCB trace is directly proportional to the length of the trace, and inversely proportional to the height and width of the trace. The equation for resistance in a uniform conductive material with a rectangular cross section is:
    where: R = trace resistance, ltrace = trace length, W= trace width, T = trace thickness (about 1 mil), and s is the conductivity of the trace material.
      copper conductivity = 5.7 x 107 ohm-meters-1
      1 mil = 1/39000 meter = 2.56 x 10-5 meter

## Slide 23
    Problem
      Calculate the parasitic resistance of a PCB trace that is 15 inches long, 1 mil thick, and 20 mils wide.
    Solution:
      First we convert all units of length into meters:
      L = 15 inches * (1 meter / 39 inches) = 0.38462 meters
      T = 1 mil * (1 meter / 39370 mils) = 2.54 x 10-5 meters
      W = 20 mil * (1 meter / 39370 mils) = 5.08 x 10-4 meters
      Applying the previous equation to a copper trace, we get a total parasitic resistance of:


## Slide 24
DIB Traces, Shields and Ground
  Trace Inductance
    The inductance of a DIB trace depends on the shape and size of the trace, as well as the geometry of the signal path through which the currents flow to and from the load impedance. The figure below shows a signal source feeding a load impedance through a pair of signal lines. In this example, the current is forced to return to the source through a dedicated current return line. The signal line and the current return line form a loop through which the load current flows.
Signal
Source
Signal Path
Current Return Path
Load Current
Load Impedance
ZL

## Slide 25
Signal
source
Load current
Load impedance
ZLOAD
Parasitic inductance of signal path
In reality, ground plane is solid ground, but signal path is a long trace that act as an inductor

## Slide 26
DIB Traces, Shields and Ground
  Trace Inductance
    We wish to minimize the effects of parasitic trace inductance on the DUT and DIB circuits. There are a number of ways to reduce this inductance.
      Minimize the area enclosed by the load current path.
      One easy way to do this is to lay a dedicated current return trace along side the signal trace. Another way to obtain low inductance is to use a solid ground plane as the return path for all signals.
      By routing each signal trace over a solid ground plane close in the stack up, thus the load current can return underneath the trace along a path with very low cross sectional area.
      Another way to reduce inductance is to make the trace as wide as is practical, since a wide trace over a ground plane has minimal inductance.

## Slide 27
DIB Traces, Shields and Ground
  Trace Inductance
      The inductance of a trace over a ground plane is dominated by the ratio of the trace-to-ground spacing, D, divided by the trace width, W .
      The parasitic inductance of a wide trace routed over a ground or power plane can be estimated using the equation:
        Ll = Inductance per unit length (Henrys per meter)
        mo = magnetic permeability of free space (400p nH per meter)
        mr = magnetic permeability of the PCB material divided by mo
W
D
T

## Slide 28
D / W ratio
0.1
0.01
1
10
10 mH/m
100 mH/m
1 mH/m
100 nH/m
10 nH/m
Trace
inductance per unit length, Ll
Crude estimate using Eq. above
Refined estimate (fringe effects included)
W
D
T

## Slide 29
DIB Traces, Shields and Ground
  Trace Inductance
      The value of mr is very nearly equal to 1.0 in all common PCB materials, so we can drop it from our calculations. The total inductance of the trace is directly proportional to the length of the trace:
      where
        L = total inductance and ltrace = trace length (meters)
      Thus trace inductance increases as trace length increases and also increases as trace width decreases. Therefore, if we want to minimize parasitic inductance in PCB traces, we should make them as wide as possible, as short as possible, and as close to the ground or power plane as possible.

## Slide 30
DIB Traces, Shields and Ground
  Trace Inductance
    It should be noted that the inductance of a trace over a ground plane is the same as the inductance of a trace over a second trace of equal size and shape.
W
D
T

## Slide 31
DIB Traces, Shields and Ground
  Trace Capacitance
    The capacitance between two parallel traces can be estimated using the standard parallel plate capacitance equation. The parasitic capacitance between two metal plates of area A is given by the equation:
    Where:
      A = area of either plate
      D = distance between the plates
      eo = electrical permittivity of free space (8.8542 x 10-12 F/m)
      er = relative permittivity of the dielectric material

## Slide 32
100 pF/m
1000 pF/m
10 pF/m
1 pF/m
0.1 pF/m
Trace-to-trace
capacitance per unit length
D / W ratio
1
0.1
10
100
Crude estimate using Eq. (17.10)
Refined estimate (fringe effects included)
CL=C/Ltrace= ere0A/D /Ltrace = ere0A /Ltrace /D = ere0 W/D
W
D

## Slide 33
DIB Traces, Shields and Ground
  Trace Capacitance
    The value of er depends on the PCB insulator material.
    Air has a relative permittivity very near 1.0.
    FR4 fiberglass has a relative permittivity of about 4.5.
    Teflon, by contrast, has a relative permittivity of about 2.7.
    Therefore, Teflon PCBs exhibit less capacitance per unit area than FR4 PCBs. This is one reason that Teflon is superior for extremely high frequency applications, since it leads to lower values of parasitic capacitance.

## Slide 34
DIB Traces, Shields and Ground
  Trace Capacitance
    If W is about 10 times as large as D, then we can estimate the capacitance per unit length of the trace:
    To calculate the total capacitance between two traces, we multiply the capacitance per unit length by the trace length.

## Slide 35
DIB Traces, Shields and Ground
  Trace Capacitance
    The best form of crosstalk prevention is to simply keep the sensitive trace as short as possible.
    Another method for reducing crosstalk is to place a ground plane underneath the critical signal traces, thus preventing layer-to-layer crosstalk.
    Each of the traces would then see a parasitic capacitance to ground, but the ground plane would block the trace-to-trace capacitance altogether.
    The trace-to-trace capacitance is replaced by two parasitic capacitances to ground. This effectively shunts the offending source to ground so that it can’t inject its signal into the sensitive node.

## Slide 36
Ground planes prevent layer-to-layer crosstalk

## Slide 37
D / W ratio
1
0.1
10
100
100 pF/m
1000 pF/m
10 pF/m
1 pF/m
0.1 pF/m
Trace-to-ground
capacitance per unit length
Crude estimate
Refined estimate (fringe effects included)

## Slide 38
DIB Traces, Shields and Ground
  Trace Capacitance
    Next we consider the capacitance between two parallel traces on the same PCB layer. This configuration occurs very frequently in PCB designs, since many traces run parallel to each other for several inches on a typical DIB
    If the trace-to-trace spacing, S, is equal to or larger than the trace width, W, we can approximate this configuration as two circular wires having the same cross sectional area as the traces and having a center-to-center spacing of S+W.
W
S
T
W

## Slide 39
DIB Traces, Shields and Ground
  Trace Capacitance
    The equation for the capacitance per unit length of two circular conductors having this geometry is:
    where:
      Cl = capacitance per unit length (Farads per meter)
      eo = electric permeability of free space
      er = relative permeability of the PCB material
      W = width of the rectangular trace
      T = thickness of the rectangular trace
      S = spacing between traces

## Slide 40
Trace-to-trace
capacitance
per unit length
S / W ratio
1
10
100
1000
100 pF/m
10 pF/m
Crude estimate using book formula Eq. (15.13)
(W=10 mils, T = 1 mil)
Refined estimate

## Slide 41
DIB Traces, Shields and Ground
  Trace Capacitance
      We can reduce the effects of trace-to-trace crosstalk between coplanar traces using a ground plane. The figure below shows a pair of coplanar traces with a width of W separated from one another by a distance S and spaced a distance D over a ground plane.
W
S
T
W
D
Sensitive
Node
Interference
Source
Trace-to-Trace
Capacitance
Sensitive Node’s
Capacitance
to Ground

## Slide 42
DIB Traces, Shields and Ground
  Shielding
      Electrostatic shields can also be used to reduce coplanar trace-to-trace crosstalk. A shield is any conductor that shunts electric fields to ground so that they don’t couple into the sensitive trace in the form of crosstalk.
      The electric fields can originate from external noise sources such as radio waves or 60 Hz power line radiation, or they can originate from other signals on the DIB. The ground plane is only one type of electrostatic shield.
      Ideally, a shield should completely enclose the sensitive node. A coaxial cable is one example of a fully shielded signal path. It would be impractical to completely shield every signal on a DIB using coaxial cables. However, we can achieve a close approximation of a fully shielded signal path by placing shield traces around sensitive signal traces. This configuration is called coplanar shielding

## Slide 43
DIB Traces, Shields and Ground
  Shielding
    Coplanar shielding can reduce crosstalk between a interference source and a sensitive DIB signal. The shield trace is connected to the ground plane to provide an extra level of protection for the sensitive node. Another benefit of shield traces is that they help to reduce the coupling of electromagnetic interference such as radio and TV signals
Interference
Source
Shield
Trace
Sensitive
Node

## Slide 44
DIB Traces, Shields and Ground
  Shielding
    Sometimes, a shield trace will be routed all the way around a sensitive node.
Interference Signal
Grounded Shield Ring
Sensitive Node

## Slide 45
Shunt
capacitance
Interference signal
Driven
guard ring
Sensitive
node
Voltage follower
Interference
signal
Sensitive
node
Driven
guard ring
Parasitic load
capacitance
Driven guards:
This cap has zero V across it

## Slide 46
Transmission Lines
  Lumped Element Model
    A transmission line or stripline can be formed by parallel trace pairs (a single trace over a ground plane), or a coaxial cable. Each of these types of transmission lines behaves according to the same equations. For example, one of the key parameters of a transmission line is its characteristic impedance, defined as follows:
      Where:
        Zo = characteristic impedance of the transmission line
        Ll = trace inductance per unit length
        Cl = trace capacitance per unit length

## Slide 47
Transmission Lines
  Lumped Element Model
    Signals injected into a transmission line travel down the line at a speed determined by the inductance and capacitance per unit length. The equation for the signal velocity is:
    The total time it takes a signal to travel down a transmission line is therefore equal to the length of the line divided by the signal velocity. This time is commonly called the transmission line’s propagation delay:

## Slide 48
Transmission Lines
  Lumped Element Model
    The wavelength of a sine wave travelling down a transmission line is given by the equation:
    The period of the signal should be at least 10 times larger than the transmission line’s propagation delay before we can treat the parasitic elements as lumped rather than distributed.

## Slide 49
Transmission Lines
  Coaxial line
    The coaxial line has perfect shielding and its propagation energy does not radiate
    Commonly used to distribute RF signals from the ATE to the DIB
    generally consists of an SMA or SMP connector-type flexible cable assembly allowing flexible routing and easy access for debugging
where
D : diameter of the braided conductor
d: diameter of the inner conductor

## Slide 50
Transmission Lines
  Stripline
    realized in printed circuit boards by placing the RF line symmetrically in between two parallel ground planes
    allows for low cost integrated passive load board elements, like directional couplers and filters
    most commonly used when high signal integrity is required
    A minor disadvantage is that striplines are not accessible for matching, and any access to this line will be made with a via, which is a discontinuity in itself
    Line Impedance can be calculated using tools like LINECALC of the Agilent EESOF package, AWR’s TXLINE, or Ansoft’s TRL to name a few

## Slide 51
Transmission Lines
  Microstrip Line
    open center conductor trace on the top layer of the PCB just above a ground plane
    most commonly used transmission line geometry for RF DIB
    allows easy access for debugging purposes, and allows for the addition of components to tune the RF performance when necessary
    One significant difference between the microstip line and the stripline, and coaxial line configuration is that the dielectric medium through which the electromagnetic wave is traveling is not homogeneous, since parts of the EM-wave will be in the PCB board with dielectric constant and the other part will be in the free air space above the line, which causes different phase velocities and wavelengths. This effect is called dispersion

## Slide 52
Transmission Lines
  Coplanar waveguide (CPW)
    A CPW is formed from a conductor separated from a pair of adjacent ground planes
    A variance of the CPW is a grounded coplanar waveguide (GCPW), where a ground plane is positioned on the opposite site of the substrate
    An advantage of CPW is that it provides an extremely high frequency response, as it uses no vias in the ground path
CPW
GCPW

## Slide 53
Transmission Lines
  Transmission line calculator LineCalc

## Slide 54
Transmission Lines Discontinuities
  Every time when an EM wave hits a discontinuity in a transmission line, the RF current will crowd which will behave like an inductor, or the electrical field will fringe which has a capacitance nature.
  For a best and most simple design of a RF DIB it is recommended, to avoid any line discontinuities
  it is obvious, that RF lines can’t be connected in a Tee or Cross configuration without simulating this new RF element with a RF simulation
  Performance impact of line discontinuities are shown in the next slide

## Slide 55
Transmission Lines Discontinuities

## Slide 56
Transmission Lines
  Transmission Line Termination
    To understand the purpose of transmission line termination, let us first examine the behavior of an unterminated line. An unterminated transmission line behaves as a sort of electronic echo chamber. If we transmit a stepped voltage down an unterminated transmission line, it will bounce back and forth between the ends of the line until parasitic resistance in the line eventually causes the echoes to die out. The resulting reflections appear as undesirable ringing on the stepped signal. Properly chosen termination resistors placed at either the source side or the load side of a transmission line cause it to behave in a much simpler manner than it would behave without termination. The purpose of termination resistors is to dissipate the energy in the transmitted signal so that reflections do not occur.

## Slide 57
Transmission Lines
  Transmission Line Termination
    If the termination resistor RT is equal to the characteristic impedance of the transmission line, then the transmitted signal will not reflect at all. The energy associated with the currents and voltages propagating along the transmission line is completely dissipated by the termination resistor. As far as the signal source is concerned, a terminated transmission line looks just like a resistor whose value is equal to Zo. The distributed inductance and capacitance of the transmission line completely disappear as far as the source is concerned.
      The only difference between a purely resistive load and a terminated transmission line is that the signal reaching the termination resistor is delayed by the propagation delay of the transmission line. Also it is important to note that while the termination resistor is usually connected to ground, it can be set to any DC voltage and the transmission line will still be properly terminated.

## Slide 58
Termination
Resistor,
RT=Zo
DUT
Output
Transmission Line, Characteristic
Impedance = Zo
Tester Instrument and Connecting Cable
Termination
Resistor,
RT=Zo
DUT
Output
Equivalent Load
Series
Resistor, RS
Series
Resistor, RS

## Slide 59
Transmission Lines
  Transmission Line Termination
    The ability to treat a terminated transmission line as a purely resistive element is very useful. Many tester instruments are connected to the DUT through a 50 W transmission line which is terminated with a 50 W resistor at the instrument’s input (on the previous slide). As far as the DUT is concerned, this instrument looks just like a 50 W resistor attached between its output and ground. If the DUT output is unable to drive such a low impedance, then we can add a resistor, RS, between the DUT output and the terminated transmission line. The DUT output then sees a purely resistive load equal to RS+Z0. The signal amplitude is reduced by a factor of Z0/(Z0+RS), but we can compensate for this gain error using a calibration factor.

## Slide 60
Transmission Lines
  Transmission Line Termination
    If we observe the signals at the DUT output, the input to the transmission line, and the input to the tester instrument, we can see the effects of the resistive divider and the propagation delay of the transmission line. The signal is attenuated by the series resistor and termination resistance, and it is also delayed by a time equal to Td.
DUT
Output
Transmission
Line Input
Tester
Instrument
Input
Td

## Slide 61
Transmission Lines
  Transmission Line Termination
    One of the common mistakes made by novice test engineers is to observe the output of a digital channel at the point where the DIB connects to the test head. Such an observation point represents an intermediate point along the cascaded transmission line. As a result, a rising edge will appear as a pair of transitions rather than a single transition. The novice test engineer often thinks the tester driver is defective, when in fact it is working just fine. The only way to see the correct signal is to observe it at the DUT’s input.

## Slide 62
Transmission Lines
  Transmission Line Termination
    Notice that we can measure the propagation delay of a transmission line by measuring the time between the first and second step transitions at the source end of a source-terminated transmission line. This time is equal to 2*Td. We can divide the measured time by two to calculate the transmission line’s propagation delay. This is how modern testers measure the propagation delays from the digital channel card drivers to the DUT’s digital inputs. The tester can automatically compensate for the electrical delay in each transmission line, thereby removing timing skew from the digital signals. This deskewing process is known as time domain reflectometry, or TDR.

## Slide 63
Grounding and Power Distribution
  Grounding
    The term “grounding” refers to the electrical interconnection and physical layout of the various ground nodes in an electronic system such as an ATE tester and DIB.
    The Test Engineer needs to remember when placing a Ground node, that the ground path is as important as the signal path and represents the return path of the signal to the ATE or DUT
    In a circuit schematic, grounds are treated as perfect zero volt reference points exhibiting zero impedance. In a real system, there can be only one point that is defined as true ground. All other ground nodes are connected to true ground through resistive and inductive traces, wires, or ground planes. Often, these parasitic resistors and inductors play a significant role in the performance of the DUT and the ATE tester instruments.

## Slide 64
Grounding and Power Distribution
  Grounding
    One way to achieve proper grounding is to pay close attention to the flow of currents through the traces, wires, and planes in the DIB and tester. The first thing we have to consider is DC measurement errors caused by resistive drops in ground connections. The figure on the following slide shows a simple test setup including a DC current source, a DC voltmeter, and a DUT (a simple load resistor in this case). We wish to measure the value of the resistor by forcing a current, ITEST, and measuring the voltage drop across the resistor, VTEST. The resistor’s value is calculated by dividing VTEST by ITEST.

## Slide 65
Grounding and Power Distribution
  Grounding
Load
Resistance,
RL
DUT
Test
Current,
ITEST
VTEST
Interconnecting
Cables and Traces
Ground
Resistance,
RG
Load
Resistance,
RL
Source
Resistance,
RS
Measure
Resistance,
RM
DUT
Test
Current,
ITEST
VTEST

## Slide 66
Grounding and Power Distribution
  Grounding
    Obviously, accurate mixed-signal testers can not be constructed using such a simple grounding scheme. Instead, they use a signal which we will call device ground sense, or DGS, to carry the DUT’s 0 Volt reference back to each tester instrument. Since the DGS signal is carried on a network of zero-current wires, the series resistances of these wires do not result in voltage measurement errors. Any number of tester instruments can use the DGS line as a zero volt reference, provided that they do not pull current from DGS. Consequently, each tester instrument typically contains a high input impedance voltage follower to buffer the voltage on DGS.

## Slide 67
Grounding and Power Distribution
  Grounding
    The DGS signal is often routed all the way to a point near the DUT which serves as the true 0 Volt reference point of the entire test system. This single point is known by several names, including star ground and device zero. We will use the term “device zero”, or DZ, to refer to this point in the circuit. All measurement instruments should be referenced to the DIB’s DZ voltage.
RG
Load
Resistance,
RL
RS
RM
DUT
Test
Current,
ITEST
VTEST
RM
Device Ground Sense (DGS) Line
Device Zero (DZ)

## Slide 68
Grounding and Power Distribution
  Power Distribution
Source 1
Source 2
Source 3
HF
HS
LF
LS
HF
HS
LF
LS
HF
HS
LF
LS
DC Meter
Digitizer
DIB
DUT
DZ
IN+
IN-
IN+
IN-
DGS Line

## Slide 69
Grounding and Power Distribution
  Power Distribution
DUT
Analog Ground
DUT
Power Supply Pin
DZ
Power Supply #1 High Force
Power Supply #1 High Sense
Power Supply #1 Low Force
DGS Line
Instrument XYZ Low Force
a) Proper Connections
DZ
Power Supply #1 High Force
Power Supply #1 High Sense
Power Supply #1 Low Force
DGS Line
Instrument XYZ Low Force
b) Improper Connections

## Slide 70
Grounding and Power Distribution
  Power and Ground Planes
    The ground plane provides a low inductance connection between all the grounds on a DIB. Similarly, power supplies can be routed using power planes to reduce the series inductance between all power supply nodes. Power and ground planes can be divided into sections, forming what are known as split planes. Each section of a split plane can carry a different signal, such as +12 V, +5 V, and –5 V. This provides the electrical superiority of copper planes without requiring a separate plane for each supply. Typically, power is applied through split planes while grounds are connected to solid (non-split) planes.

## Slide 71
Grounding and Power Distribution
  Power and Ground Planes
    There are usually at least two separate ground planes in any mixed-signal DIB. One plane forms the ground for the transmission line traces carrying digital signals. This plane is subject to rapidly changing current flows from the digital signals, and therefore exhibits fairly large voltage spikes caused by the interactions of the currents with its own inductance. This ground plane is often called DGND (digital ground) in the DIB schematics.
    The second plane, AGND (analog ground), is for use by analog circuits. Ideally, this plane should carry only low frequency, low current signals that will not give rise to voltage spikes.

## Slide 72
Grounding and Power Distribution
  Power and Ground Planes
    A third plane is sometimes used as a DIB-wide zero volt reference. This “quiet ground” plane (QGND) can be used by any analog circuits on the DIB that need a low noise ground reference. This plane must be connected in such a way that it does not carry any currents exceeding a few milliamps. It should be tied only to the DZ node at a single point and to relatively high impedance DUT pins and DIB circuit nodes. Often, the analog ground plane and the quiet ground plane are combined into a single plane, resulting in a DIB with only two ground planes (analog and digital).

## Slide 73
Grounding and Power Distribution
  Power and Ground Planes
Layer 1 (Digital Signals)
Layer 2 (DGND Plane)
Layer 5 (QGND Plane)
Layer 6 (Analog Signals)
DUT
DGND
Pin
Layer 3 (Split Power Plane)
Layer 4 (AGND Plane)
DUT
AGND
Pin
DIB Circuit
Ground Input
(High Impedance)
DZ
DUT
+5V
Pin
AGND to DGND
Connection
(Single Point)
Power Plane
Split

## Slide 74
Grounding and Power Distribution
  Ground Loops
    A star grounding scheme is formed by connecting the grounds of multiple circuits to a single ground point, rather than connecting them in a daisy chain. Star grounds prevent a common grounding error known as a ground loop. A ground loop is formed whenever the metallic traces and wires in a ground network are connected so that a loop is formed.
    A fluctuating magnetic field passing through a loop of wire gives rise to a fluctuating electric current in the wire. The fluctuating current, in turn, gives rise to a fluctuating voltage in the wire due to the wire’s series resistance and inductance. Thus, AC voltages can be induced into ground wires if we carelessly connect them in a loop.

## Slide 75
Grounding and Power Distribution
  Ground Loops
    Ground loops are most commonly formed when we connect instruments such as oscilloscopes and spectrum analyzers to our DIB (as seen on the next slide). The tester housing and its electrical ground must be connected to earth ground for safety reasons to prevent electrical shock. Likewise, an oscilloscope’s housing and electronics must be connected to earth ground.
    The ground loop often causes the tester’s signals to appear terribly corrupted with 60 Hz power and other noise components. The test engineer has to realize that these signals are not present in the tester itself. They disappear as soon as we disconnect the bench instrument.

## Slide 76
Grounding and Power Distribution
  Ground Loops
Tester
Safety
Ground
Ground
Loop
Tester
Instrument
Ground
Tester
Mainframe
Bench
Instrument
Safety
Ground
Earth
Ground
Test Head
and DIB
Bench
Instrument
Instrument
Probe

## Slide 77
Grounding and Power Distribution
  Improving the cross coupling path via GND by increasing the signal length

## Slide 78
DIB Components
  DUT Sockets and Contactor Assemblies
    The DUT pins and the circuit traces on a DIB must be connected temporarily during test program execution. A hand-test socket or a handler contactor assembly makes the temporary connection. The most important thing to note is that the metallic contacts of the socket or contactor assembly represent an extra resistance, inductance, and capacitance to ground that will not exist when the DUT is soldered directly to the PCB in the customer’s system-level application.
    Sometimes the parasitic elements are unimportant to a device’s operation, but other times, particularly at high frequencies, they can be extremely critical.

## Slide 79
DIB Components
  Contact Pads, Pogo Pins, and Socket Pins
    Contact pads are metal pads formed on the outer trace layers of a DIB PCB. They appear on DIB schematics as circles, black dots, or connector bars. These pads allow a relatively non-abrasive connection between one layer of interface hardware and the next. Two common uses for connector pads are pogo pin connections and DUT socket pin or contactor pin connections. A pogo pin is a spring-loaded gold-plated rod that provides a connection between two connector pads. Pogo pins may have blunted ends, pointed ends, or crown-shaped ends, depending on the connection requirements. Pointed or crown-shaped ends tend to dig into the pad surface, providing a reliable, low resistance connection to the pad. However, the digging action may eventually destroy the pad. Blunted pogo pins are less abrasive to the pads, but are slightly less reliable since they don’t dig into the pad surface.

## Slide 80
DIB Components
  Contact Pads, Pogo Pins, and Socket Pins
Socket Pad
Socket Pin
PCB Trace
Spring-Loaded
Pogo Pin
Pogo Pad
DUT

## Slide 81
DIB Components
  Contact Pads, Pogo Pins, and Socket Pins
    A connection formed with a contact pad can be treated as an ideal zero impedance connection in most cases.
    Pogo pins and socket pins also add inductance to the signal path. The inductance may be as little as one nH or as large as a few tens of nH. In general, long thin pins add more inductance than short fat ones. Socket pins and pogo pins may also introduce pin-to-pin or pin-to-ground parasitic capacitance on the order of a few pF.
    You seldom can control the size of the current loop, therefore you are basically left with selecting the appropriate socket with short pins.

## Slide 82
DIB Components
  Example specification of a high performance test socket

## Slide 83
DIB Components
  Electromechanical Relays
    One of the more common DIB components used in mixed-signal testing is the electromechanical relay. The relay is an electromagnetically controlled mechanical switch.
    Relays allow the DIB circuits to be appropriately reconfigured for each measurement in the test program. As one of the few moving parts on a DIB, relays represent a potential reliability problem in production.
    The metal contacts in a relay are pulled open or closed using an electromagnetic field generated by a DC current passing through a coil of wire. The current is switched on or off under test program control as the test code is executed.
    Flyback diodes are sometimes added to the DIB in parallel with each relay coil to prevent the coil’s inductive kickback voltage from damaging the current-driving electronics located inside the tester.

## Slide 84
DIB Components
  Electromechanical Relays
Case
Wiper
Posts
Coil
Mechanical Diagram
Schematic Symbol
Pole

## Slide 85
DIB Components
  Electromechanical Relays
    In conventional relays, the moving armature is called the wiper. Since it pivots on its pole, it may eventually wear out and get stuck. A more reliable relay is the reed relay, which uses two springy metal reeds that become magnetized by the coil’s electromagnetic field. They are attracted to each other by the induced magnetism. Since the reeds do not swing on any pivot, there are no parts to wear out other than the point of contact between the two reeds. Reed relays are used very often on DIBs because of their superior reliability.
    Damage can also be caused to the wiper and contacts by abrupt changes in the current passing through the contacts as they open and close. The high di/dt current changes can induce large inductive voltage spikes, leading to a spark that welds the contacts together.

## Slide 86
DIB Components
  Electromechanical Relays
    Relays, like manually activated switches, are available in a variety of configurations. The most common versions are single-pole/single-throw (SPST), single-pole/double-throw (SPDT), double-pole/single-throw (DPST), and double-pole/double-throw (DPDT). The schematic representation of each of these configurations is shown below.
SPST
DPST
SPDT
DPDT

## Slide 87
DIB Components
  Electromechanical Relays
    The parasitic behavior of relays may exhibit a number of possible non-ideal characteristics, including series resistance through the wiper and posts (RWP), series inductance through the wiper and contacts (LW), inductive coupling between the contacts and ground (CPG), capacitive coupling between the wiper and the coil (CWC), capacitive coupling from contact to contact, and mutual inductance between the coil and the wiper.
    Series resistance is typically only a few hundred mW, although the exact value changes from one closure to the next.
    Series inductance is often fairly high, and may exceed 10 mH.
    Capacitance values are usually around 1 to 5 pF.

## Slide 88
DIB Components
  Solid State Relays (or FET switch)
    Highly reliable relay based on FET switch without any mechanical part
    Solid state FET switches are LED driven MOS FET driver which have an ON-Resistance as low as 1 Ohm and an output capacity of 1 pF or less
    Since the solid state FET switch has no mechanical parts, it can be build extremely small and can achieve hundreds of millions switching cycles

## Slide 89
DIB Components
  Resistors
    Resistors are available in a variety of package types, including surface mount, axial leaded, and non-axial leaded varieties. They can be constructed using a wide variety of resistive materials, most commonly carbon or metal (e.g. aluminum). Resistors can be constructed either as a solid core of resistive material, a coil of resistive wire, or a thin film of resistive carbon or metal.
Axial Leaded
Non-Axial Leaded
Surface Mount
(Chip Resistor)

## Slide 90
DIB Components
  Resistors
    Considerations in resistor selection include:
      Size
      Power dissipation
      Precision
      Cost is inversely proportional to precision
      Ideal performance of the resistor (does it show a large series inductance?)
Typical |Z|/R-ratio for a 50 Ω-resistors

## Slide 91
DIB Components
  Capacitors
    Capacitors suffer from a number of parasitic elements. The dielectric material can be slightly conductive, giving rise to an effective high-value resistance, RP, in parallel with the capacitor’s plates. This leads to current leakage from one plate to the other whenever the capacitor is charged. The capacitor’s leads and plates also contribute series inductance, LS, and series resistance, RS. Thus, a simple parasitic model of a physical capacitor including dielectric leakage and parasitic series resistance and inductance is shown below.
Cross section of a multilayer chip capacitor

## Slide 92
DIB Components
  Capacitors
Equivalent Series Inductance: ESL; Equivalent Series Resistance: ESR
Quality factor with
Self Resonance Frequency
Package | Size [mm] | ESL [pH]
0201 | 0.6x0.3 | 400
0402 | 1x0.5 | 550
0603 | 1.6x0.8 | 700
0805 | 2.0x1.25 | 800
1206 | 3.2x1.6 | 1250
0612 | 1.6x3.2 | 63
Common SMD Capacitor size and ESL values
Capacitor type | value | ESL [pH]
Leaded disc ceramic | 0.01 mF | 3000
Leaded monolithic ceramic | 0.01 mF | 1600
Leaded monolithic ceramic | 0.1 mF | 1900
SMD aluminum electrolytic | 47 mF | 6800
SMD tantalum electrolytic | 47 mF | 3400
Typical ESL values for leaded and electrolytic capacitors

## Slide 93
DIB Components
  Capacitors

## Slide 94
DIB Components
  Inductors and Ferrite Beads
    Inductor are occasionally required as part of a DUT circuit such as a voltage doubler.
    They may also be used as part of a passive load circuit that must be connected to a DUT output to simulate a speaker coil or similar system-level component.
    Inductors can also be used in conjunction with capacitors to simulate long transmission lines by building an LC network.
    Inductors are used as part of an RF matching circuit
    Inductors can be modeled as an inductance in series with a resistance.

## Slide 95
DIB Components
  Inductors and Ferrite Beads
    Depending on the magnetic core material chosen, the inductor may also exhibit lossy behavior at high frequencies, resulting in an apparent increase in the series resistance of the coil wire.
    In fact, a class of inductors called ferrite beads are intentionally designed with very lossy core materials to achieve a component with near-zero resistance at low frequencies and higher resistance at higher frequencies.
    Ferrite beads are useful for blocking high frequency interference signals. They can reduce AC crosstalk from one circuit to another, while allowing DC current to flow freely.

## Slide 96
DIB Components
  Inductors and Ferrite Beads
    Self resonant frequency:
Typical ferrite bead impedance chart
Typical inductance and impedance for a 100 nH wire wound inductor

## Slide 97
DIB Components
  Inductors and Ferrite Beads
    For example, a ferrite bead can be placed in series with a power supply to prevent supply current spikes drawn by one circuit block from disturbing another circuit block. Both the inductance and resistance of the bead are near zero at DC, so power supply current can flow freely through the ferrite beads.
Circuit 1
VDD
Circuit 1
VDD
Ferrite Beads
Decoupling Caps
VDD

## Slide 98
DIB Components
  Transformers and Power Splitters
    Transformers are sometimes used on DIBs to translate a high-frequency single-ended signal into a differential signal or vice-versa.
    Unfortunately, the transformer’s frequency response is highly dependent on the output impedance of the transmitting circuit as well as the input impedance of the receiving circuit.
    Consequently, the frequency response of the transformer is difficult to accurately calibrate, since it may change from one DUT to the next.

## Slide 99
DIB Components
  Transformers and Power Splitters
    Power splitters are controlled impedance transformers that are useful at high frequencies.
    They are typically used in RF and microwave systems, but occasionally find use on mixed-signal DIBs.
    Power splitter and transformer operation are sometimes limited to a small range of frequencies depending on the internal circuits
    Transformers and power splitters, by contrast, present a low impedance inductive or resistive load the DUT. Since many DUTs can’t drive low impedances, transformers and power splitters are often unusable.
    However, because they can handle frequencies well above those handled by active op amp circuits, they are sometimes the only viable choice

## Slide 100
DIB Components
  Matching Circuits for RF Boards
  The term matching means the impedance transformation, in terms of ATE it means in the most cases to transform the input impedance of the DUT to the port impedance of the ATE which his in most cased 50W.
  In principle there kinds of matching
    The conjugate Match transforms the load impedance ZL to the conjugate match of the source impedance ZS with ZS = ZL*. This type of matching will maximize the power delivery to the load, but will not minimize the reflections unless ZS is real.
    The load match transforms the load impedance ZL to the line impedance Z0. This matching is minimizing the reflections but does not maximize the delivered power unless Z0 is real. The load matching is best used at ends of transmission lines.
    The functional match which will load the device with an impedance that optimize the performance. This match is done e.g. when optimizing the noise figure of an LNA since the best noise performance does not require necessarily the same load impedance than the best gain or power performance.

## Slide 101
Introduction to the Smith Chart

## Slide 102
Introduction to the Smith Chart

## Slide 103
Introduction to the Smith Chart
  The input impedance ZIN of a loss less line with the impedance ZTL which connects complex load impedance ZL is given by
or normalized:

## Slide 104
Introduction to the Smith Chart
  Admittance Smith Chart

## Slide 105
Introduction to the Smith Chart
  Immitance Smith Chart
-1
1
-0.2
-0.4
-0.6
-2
-5
0.2
0.4
0.6
1
2
5
0.2
0.4
0.6
1
2
0.2
0.4
0.6
2
5
-0.2
-0.4
-0.6
-1
-2
-5
0.2
0.4
0.6
2
10
20
30
40
50
60
70
80
90
170
160
150
140
130
120
110
100
180
-90
-160
-150
-140
-130
-120
-110
-100
-170
-20
-30
-40
-50
-60
-70
-80
-10
0
0
0.5
1.0
-0.5
-1.0
z=0
g=0
The impedance grid is shown here in black, the admittance grid in gray.

## Slide 106
Introduction to the Smith Chart

## Slide 107
Introduction to the Smith Chart
z=0+j0
1
-1
1
z=∞
Inductive reactance (positive)
Capacitive reactance (negative)
open circuit
short circuit
Reference impedance z=1+j0
Ideal resistance x=0
Constant resistance circles
Constant reactance arcs

## Slide 108
Introduction to the Smith Chart
g=0
-1
1
1
g=∞
Inductive susceptance (negative)
Capacitive susceptance (positive)
short circuit
open circuit
Reference admittance y=1+j0
Ideal conductance b=0
Constant conductance circles
Constant susceptance arcs

## Slide 109
Introduction to the Smith Chart

## Slide 110
Introduction to the Smith Chart
  Illustrative Example for parallel capacitor

## Slide 111
Introduction to the Smith Chart
  Illustrative Example for parallel inductor

## Slide 112
Introduction to the Smith Chart
  Illustrative Example for parallel resistor

## Slide 113
Introduction to the Smith Chart
  Illustrative Example for series capacitor

## Slide 114
Introduction to the Smith Chart
  Illustrative Example for series capacitor

## Slide 115
Introduction to the Smith Chart
  Illustrative Example for series resistor

## Slide 116
Introduction to the Smith Chart
  Impedance Matching with a series and shunt component

## Slide 117
Introduction to the Smith Chart
  Impedance Matching with a series and shunt component

## Slide 118
Common DIB Mistakes
  Poor Power Supply and Ground Layout
    One of the most common sources of noise injection in mixed-signal DIBs is poor power and ground layout.
    The best way to avoid problems with power distribution and grounding is to use as many planes as needed, without regard to DIB cost. Although each layer in a multilayer DIB adds fabrication cost, the expense is fairly negligible compared to the production yield loss due to poor DIB performance.
    A good DIB should include:
      one or two layers dedicated to digital transmission line ground and noisy current returns,
      one layer dedicated to analog current returns,
      one layer dedicated to low-current analog ground
      and at least one layer dedicated to split power planes.

## Slide 119
Common DIB Mistakes
  Crosstalk
    Another common problem on mixed-signal DIBs is crosstalk, especially between digital and analog signal lines. The digital-to-analog crosstalk problem can be reduced by placing analog signals on a separate layer from digital signals, with an analog ground plane between the two layers.
    Sensitive nodes should be as short as possible to avoid crosstalk and coupling of external noise sources.
    One of the most common sensitive nodes on a mixed-signal DUT is its current reference input. This input is typically tied to VDD or ground through a very high impedance bias resistor. The node between the bias resistor and the DUT is an extremely sensitive one. Noise injected into this node will translate directly into noise throughout the DUT. Therefore current bias nodes should always be kept extremely short, preferably surrounded by a shield ring.

## Slide 120
Common DIB Mistakes
  Transmission Line Discontinuities
    Small discontinuities in transmission lines can lead to glitches on the rising and falling edges of very fast digital signals.
    Such glitches can sometimes lead to timing errors or double clocked logic in the DUT.
    The discontinuities are caused by lumped capacitance or inductance at transition points along the transmission line. For example, a lumped capacitance and/or inductance exists whenever a digital signal trace is routed between layers through a via or other through hole.
    Avoid routing digital signals from one layer to another, unless absolutely necessary.

## Slide 121
Common DIB Mistakes
  Resistive Drops in Circuit Traces
    Even relatively short traces may have a series resistance of several hundred milliohms. If we try to force current through such a trace, we will get a voltage drop due to the parasitic resistance of the trace. Sometimes these voltage drops are unimportant, but other times they can lead to errors nearly as large as the parameter we are trying to measure.
    If the series resistance is serious enough to cause a problem, the trace can either be made wider, or a sensing circuit such as a Kelvin connection can be used to compensate for the resistive drops in the PCB trace.

## Slide 122
Common DIB Mistakes
  Tester Instrument Parasitics
    The various cables and wires that connect a DUT to a tester’s instruments can present a significant capacitive load to the DUT’s pins. Often, the loading is high enough to cause gain errors, phase shifts, or even DUT circuit oscillations. It is very important for a test engineer to ask the design engineer responsible for each DUT circuit what its capacitive drive capabilities will be.
    If the output impedance of the DUT is incompatible with the tester’s load capacitance, then a voltage follower will probably be needed on the DIB buffer the DUT’s output.

## Slide 123
Common DIB Mistakes
  Oscillations in Active Circuits
    Operational amplifiers used in buffer amplifiers or other DIB circuits may break into oscillations if they are not laid out properly.
      For example, the inverting and non-inverting inputs to an op amp are extremely sensitive to parasitic capacitance. If these traces are laid out so that they are more than a few tenths of an inch long, the amplifier will often break into oscillations.
    Another source of oscillations is poor power supply and decoupling capacitor layout. Decoupling capacitors in general should always be placed very close to their supply pin.

## Slide 124
Common DIB Mistakes
  Poor DIB Component Placement and PCB Layout
    The physical layout of the DIB is extremely critical to mixed-signal DUT performance.
    Short traces have less parasitic resistance, inductance, and capacitance than long traces. The best way to achieve short PCB traces is to arrange the DIB components in a way that allows short traces, especially in critical nodes.
    Component placement, power and ground schemes, trace layout, and other physical decisions must be made with knowledge of the DUT and DIB circuits and their required performance.

## Slide 125
Summary
    A good DIB is one of the most critical elements in a successful mixed-signal test solution. Without good DIB performance, the DUT may be unable to meet its specifications, regardless of the quality of the test code. Many things lead to good mixed-signal DIB design, including proper component selection and placement, proper power and ground layout, proper PCB stackup, and proper attention to parasitic components related to PCB traces and DIB components.
    It is critical for the test engineer to review his test plan and DIB design with the design engineers before the DIB is laid out and fabricated. Otherwise, the DIB may turn out to be an expensive but useless piece of test hardware, proving once again that concurrent engineering is critical to mixed-signal product development.