## Slide 1: Test Time Reduction With SATOM Simultaneous AC-DC Test with Orthogonal Multi-excitation
Degang Chen, Zhongjun Yu
Iowa State University
Krunal Maniar, Mojtaba Nowrozi
Texas Instruments
2014 IEEE Ned Kornfield Best paper Award

## Slide 2: Purpose
Final test time for precision analog and mixed-signal IC is long and is a major portion of total manufacturing cost
The proposed SATOM test strategy will
  Reduce test time by well over 90%
  Provide better coverage
  Achieve the same test accuracy

## Slide 3: Outline
Introduction
The SATOM concept
The SATOM test procedure
Measurement results and comparison
Conclusion

## Slide 4: Introduction
Precision AMS IC’s require high-precision measurements in final test
Each measurement needs accurate and slow settling
There are many AC/DC specs to be tested
Leading to long test time on expensive test equipment
 large test cost

## Slide 5: Introduction
An ADC is an multi input multi output device
  Input: Vip, Vin, Vrefp, Vrefn, AVDD, AVSS, DVDD, …
  Output: Dout, busy, ready, …
  Critical output: Dout
ADC
Dout
AVDD
AVSS
DVDD
Vicm+Vid/2
Vnoise
Vicm-Vid/2

## Slide 6: Introduction
All input can cause response at Dout
Since ADC is ratio-metric, ignore Vrefp, Vrefn
Ideally, the interpreted output should be
But actually, we have

## Slide 7: Introduction
State of the art ADC testing:
  Sequentially apply stimuli, measure Dout
ADC
Dout
AVDD
AVSS
DVDD
Vicm
AC Vid
DC Vid
DSP
Complicated setup and long test time

## Slide 8: The SATOM Concept
Simultaneously apply multiple excitations
CM and supplies at nominal values
Vid large signal, all D’s small signals
All signals are orthogonal sinusoids
ADC
Dout
AVdd+D1
AVss+D2
DVdd+D3
Vicm+D4+Vid/2
Vicm+D4-Vid/2
noise
Vid
Vicm+D4

## Slide 9: The SATOM Concept
Orthogonal signals
Sinusoidal signals of different frequencies are orthogonal over their common period

## Slide 10: The SATOM Concept
Select Vid and Di’s to have different freq
Make data record length common period
Make sure harmonic distortions of Vid and intermodulation between Vid and Di’s all have different frequencies
 Vid, Di’s, all H.D.’s, and all IMD’s are mutually orthogonal over data record

## Slide 11: The SATOM Concept
Collect a set of output over the common period under multi-excitation

## Slide 12: The SATOM Concept
Use inner products to computer coefficients
where xi is any of Vid, Di’s, H.D.’s, or IMD’s
For example, if xi = Vid, we have
From this, gain error is computed
Similarly, all other coefficients on last slide can be computed
All inner products by FFT efficiently

## Slide 13: SATOM Test Procedure
Select orthogonal multi-excitation frequencies
  Use a spreadsheet
  Select #samples in data record, M
  Select different integers J’s as #periods for each excitation
  Check with spreadsheet that all excitations, all hd and all imd after aliasing are in distinct bins with sufficient separation
   all these are coherently sampled

## Slide 14: SATOM Test Procedure
Compute signal frequencies by
Collect M samples
Use FFT to compute all coefficients
Convert results into specifications
Computation steps are described in detail in the paper, illustrated with examples

## Slide 15: SATOM Test Procedure
A word of caution
  With great effort in selecting coherent orthogonal frequencies,
  Actual generated signal may not be perfectly coherent
  In this case, use an FFT algorithm that handles non-coherent sampling
  Such as our ITC’11 or TIM’13 papers

## Slide 16: SATOM Test Procedure
Identify and remove Vid fundamental

## Slide 17: SATOM Test Procedure
Identify and remove CM signal fundamental

## Slide 18: SATOM Test Procedure
Identify and remove IM2’s due to Vid*Di

## Slide 19: SATOM Test Procedure
Remove of IM3, IM4, …, the green spikes

## Slide 20: Measurement Results
Measurement results obtained at TI
High resolution DS ADC used
Main focus on INL, the most time consuming
Repeatability established for fixed device
Robustness across multiple good/ marginal / bad devices
Accuracy measured against bench test
Time reduction against production test

## Slide 21
Repeated INL measurements, a good device
Black: 4096 point SATOM; Red: 21 point bench

## Slide 22
Repeated INL measurements, a bad device
Black: 4096 point SATOM; Red: 21 point bench

## Slide 23
Blue: 1024 point SATOM; Red: 21 point bench
Good Device 1, 10 INL curves
Good Device 2, 10 INL curves
Good Device 3, 10 INL curves
Good Device 4, 10 INL curves
Good Device 5, 10 INL curves

## Slide 24
Blue: 1024 point SATOM; Red: 21 point bench
Bad Device 1, 10 INL curves
Bad Device 2, 10 INL curves
Bad Device 3, 10 INL curves
Bad Device 4, 10 INL curves
Bad Device 5, 10 INL curves

## Slide 25
Specification | New method | Standard method | Final Test
ADC Offset | 1.0741 mV | 1.076 mV | yes
Vindiff g.e. | -5.98% | -5.98% | yes
Vindiff gain | -0.54 dB | -0.54 dB | 
AVdd PSR | -110.96 dB | -112 dB | yes
AVss PSR | -88.19 dB | -88.5 dB | yes
DVdd PSR | -117.12 dB | -115 dB | 
Vicm reject | -107.17 dB | --- | yes
Noise rms | 3.97 uV | 4uV | yes
SNR(toFS) | 112.51 dB | 112.5 dB | 
THD(toFS) | -109.28 dB | -109 dB | 
SFDR(toFS) | 113.35 dB | 113 dB | 
SNDR(toFS) | 107.59 dB | 107.3 dB | 
ENOB(SNDR) | 17.61 bit | 17.6 bit | 
Maximum INL | 4.36 ppm (1024pts) | 4.7 ppm | Yes (11 pts)
Total time | 1 sec | (long) | 
Quad test | < 0.3 sec | N.A. | > 14 sec
Comparison of test results:
Excellent match with bench test in all parameters.

## Slide 26: Additional benefits of SATOM
INL measured at many more points
INL curve available
Output power measured
Intermodulation (IM2, IM3, …) between differential input and AVDD measured
Intermodulation (IM2, IM3, …) between differential input and AVSS measured
Intermodulation (IM2, IM3, …) between differential input and DVDD measured

## Slide 27: Conclusion
Presented SATOM concept and algorithm
It uses orthogonal multi-excitation with proper digital signal processing
Demonstrated with high resolution DS ADC test
Applicable to all multi-input analog and mixed-signal circuits and systems
Reduced test time by well over 90%
Improved test coverage, same test accuracy