## Slide 1: Fast and accurate linearity test for DACs with various architectures using segmented models
Shravan K. Chaganti*, Abalhassan Sheikh†, Sumit Dubey†, Frank Ankapong†, Nitin Agarwal†, and Degang Chen*
*Iowa State University, Ames, USA †Texas Instruments Inc.
2018 International Test Conference
10/31/18
Notes: The slide guide is available in the following file:
LDSlidesV21.1.ppt Slide guide for light detail on a dark background.
Note: We have saved this presentation in the older 2003 format, because PowerPoint 2003, 2007 through 2016 can read it.
For this year’s test conference we will use PowerPoint (Office) 2016 in our projection computers.

## Slide 2: Purpose
Cost of build for analog and mixed signal products
  Production test of parametric specifications
Data Converters (ADCs and DACs)
  Critical components of ICs used in control and sensing applications
  Production test time often dominates SoC test time
Focus on optimizing static linearity test time for DACs
  Architecture-aware test methods combined with best-in-class fast linearity test concepts

## Slide 3: Outline
Conventional linearity testing of DACs
Motivation for segmented testing
uSMILE for DACs
Extrapolated Reconstruction (ER) for DACs
Modifications for Interpolated DACs
Test results
Notes: The Outline slide is an outline for the major areas of your presentation -- what you’re going to talk about. You should not include the title, introduction or conclusion in your outline. Just highlight the major areas of your talk.
The outline slide you are seeing is an outline for our ITC presentation guide.

## Slide 4: Outline
Conventional linearity testing of DACs
Motivation for segmented testing
uSMILE for DACs
Extrapolated Reconstruction (ER) for DACs
Modifications for Interpolated DACs
Test results

## Slide 5: Conventional linearity testing of DACs
Sweep 0 to max code, measure the output voltages using a digitizer, subtract from end-point fit/best fit line to get INL
The digitizer: Digital Voltmeter or a higher resolution ADC with significantly better specifications.

## Slide 6: Conventional linearity testing of DACs
Multiple measurements per code to average out the noise.
  Say 0.3LSB noise
  Noise reduces by square root of number of measurements
  To reduce 3*sigma to <0.1LSB  100 measurements per code
Example:
  input codes for an 16-bit DAC
  64 measurements per code to average out noise
  Sample rate of 500KSPS
  Total data acquisition time > 8s!
Even with multisite, test time too high
Notes: Even with multi-site testing, significant test time and cost

## Slide 7: Outline
Conventional linearity testing of DACs
Motivation for segmented testing
uSMILE for DACs
Extrapolated Reconstruction (ER) for DACs
Modifications for Interpolated DACs
Test results

## Slide 8: Motivation for segmented testing
Conventional method:
  Treat INL at each code as uncorrelated
  No. of variables to estimate = No. of DAC codes
Segmented testing:
  No. of truly independent error sources<< No. of DAC codes
Example: 16-bit R-2R DAC
  No. of resistors with mismatches=2*16=32 << 2^16= 65,536

## Slide 9: Motivation for segmented testing
True: Many other sources of nonlinearity exist
Also true: non-idealities (mismatches, voltage coefficients, etc.) of a limited number of analog components determines the errors in the input output transfer curve of the DAC.
INL/DNL = func(small no. of independent errors)
For ADCs, uSMILE [1]
Same idea ported to DACs

## Slide 10: Outline
Conventional linearity testing of DACs
Motivation for segmented testing
uSMILE for DACs
Extrapolated Reconstruction (ER) for DACs
Modifications for Interpolated DACs
Test results

## Slide 11: uSMILE: ultrafast Segmented Model Identification of Linearity Errors
INL curve broken into “segments”
Assign segmented errors to MSB/ISB/LSB codes
Example: 16-bit DAC segmented as 6-5-5
010110 11001 00110
ISB errors

## Slide 12: uSMILE
Measure voltage at code C
Preliminary “noisy” errors at M codes
equations (one for each code)
Unknowns:

## Slide 13: uSMILE
Write all equations in matrix form
Equation for one code
“noisy” errors at all codes
Coefficient matrix
(0s and 1s)
Unknowns

## Slide 14: uSMILE
The unknowns vector estimated using least squares as:
where
Full code “noise-free” INLs :

## Slide 15: uSMILE
The “time-saving-factor”
Example: for a 16-bit DAC with 8-4-4 segmentation
Estimation error: uSMILE with 1 measurement per code conventional method with 228 measurements per code

## Slide 16: Outline
Conventional linearity testing of DACs
Motivation for segmented testing
uSMILE for DACs
Extrapolated Reconstruction (ER) for DACs
Modifications for Interpolated DACs
Test results

## Slide 17: Extrapolated Reconstruction (ER)
uSMILE works because:
  Can’t we just measure these directly?
Yes, we can. Unlike an ADC, a DAC offers the opportunity to obtain the measurements for specific input codes.

## Slide 18: Extrapolated Reconstruction (ER)
Measure DAC output for
1 MSB segment (32 codes: 0,1,2,3,…,31) and
MSB points (0,32,64,….,4032,4064)
with multiple hits for each code (say 128)
“Extrapolate” and “Reconstruct” output curve
Subtract from end-point/best fit line and calculate INLs and DNLs
Example: 12-bit DAC with 7-5 segmentation
Measured voltages
Extrapolated voltages
Notes: For equivalent accuracy, total number of samples are equal for uSMILE and ER

## Slide 19: Application to various architectures
For higher resolution DACs, segmented architectures are used to avoid the exponential growth of components.
  Ex: Thermometer-binary DAC, Thermometer-R2R DAC [2]
Additionally, some architectures are inherently segmented bit-by-bit
  Ex: R-2R DAC, binary DAC

## Slide 20: Application to various architectures
For higher resolution DACs, segmented architectures are used to avoid the exponential growth of components.
  Ex: Thermometer-thermometer DAC [2]
Additionally, some architectures are inherently segmented bit-by-bit
  Ex: C-DAC

## Slide 21: Application to various architectures
Model not valid for string or thermometer-coded type architectures [2]
  Ex:15-bit DAC implemented as a 7-bit thermometer coded resistor DAC and an 8-bit R-2R DAC 7-4-4  valid 8-3-4  valid 6-5-4  invalid

## Slide 22: Simulation results for an R-2R DAC
Simulation results of a 16b R-2R DAC
(8-8 segmentation)
(tsf = 128)
(a) INL estimations using uSMILE and ER
(b) DNL estimations

## Slide 23: Simulation results for a segmented hybrid DAC
Simulation results of a 16b Segmented Hybrid DAC
(8-bit thermometer coded resistor DAC and an 8-bit R-2R DAC)
(tsf = 128)
(a) INL estimations
(b) DNL estimations

## Slide 24: Application to various architectures
Some DACs have interpolation [2]
  Reduces DNL jumps
uSMILE and ER do not account for interpolation in their model.

## Slide 25: Simulation results for an interpolated DAC
Spikes in DNL estimations at MSB codes
Simulation results of a 16b interpolated DAC
(8-bit LSB R-2R DAC interpolating between the output voltages of an 8-bit MSB string DAC) (a) INL estimations (b) DNL estimations
Notes: The DNL estimations have spikes at MSB segment transitions because interpolation is not accounted for
DNL specs are more stringent than INL
Estimation error will cause DUT to falsely fail, leading to yield loss

## Slide 26: Simulation results for an interpolated DAC
Spikes in DNL estimations at MSB codes
Simulation results of a 16b interpolated DAC
(8-bit LSB R-2R DAC interpolating between the output voltages of an 8-bit MSB string DAC) (a) INL estimations (b) DNL estimations
Notes: The DNL estimations have spikes at MSB segment transitions because interpolation is not accounted for
DNL specs are more stringent than INL
Estimation error will cause DUT to falsely fail, leading to yield loss

## Slide 27: Simulation results for an interpolated DAC
Spikes in DNL estimations at MSB codes
Simulation results of a 16b interpolated DAC
(8-bit LSB R-2R DAC interpolating between the output voltages of an 8-bit MSB string DAC) (a) INL estimations (b) DNL estimations
Notes: The DNL estimations have spikes at MSB segment transitions because interpolation is not accounted for
DNL specs are more stringent than INL
Estimation error will cause DUT to falsely fail, leading to yield loss

## Slide 28: Simulation results for an interpolated DAC
Spikes in DNL estimations at MSB codes
Simulation results of a 16b interpolated DAC
(8-bit LSB R-2R DAC interpolating between the output voltages of an 8-bit MSB string DAC) (a) INL estimations (b) DNL estimations
Notes: The DNL estimations have spikes at MSB segment transitions because interpolation is not accounted for
DNL specs are more stringent than INL
Estimation error will cause DUT to falsely fail, leading to yield loss

## Slide 29: Simulation results for an interpolated DAC
Spikes in DNL estimations at MSB codes
Simulation results of a 16b interpolated DAC
(8-bit LSB R-2R DAC interpolating between the output voltages of an 8-bit MSB string DAC) (a) INL estimations (b) DNL estimations
Notes: The DNL estimations have spikes at MSB segment transitions because interpolation is not accounted for
DNL specs are more stringent than INL
Estimation error will cause DUT to falsely fail, leading to yield loss

## Slide 30: Simulation results for an interpolated DAC
Spikes in DNL estimations at MSB codes
Simulation results of a 16b interpolated DAC
(8-bit LSB R-2R DAC interpolating between the output voltages of an 8-bit MSB string DAC) (a) INL estimations (b) DNL estimations
Notes: The DNL estimations have spikes at MSB segment transitions because interpolation is not accounted for
DNL specs are more stringent than INL
Estimation error will cause DUT to falsely fail, leading to yield loss

## Slide 31: Simulation results for an interpolated DAC
Spikes in DNL estimations at MSB codes
Simulation results of a 16b interpolated DAC
(8-bit LSB R-2R DAC interpolating between the output voltages of an 8-bit MSB string DAC) (a) INL estimations (b) DNL estimations
Notes: The DNL estimations have spikes at MSB segment transitions because interpolation is not accounted for
DNL specs are more stringent than INL
Estimation error will cause DUT to falsely fail, leading to yield loss

## Slide 32: Application to various architectures
uSMILE and ER  incorrect DNLs for interpolated DACs especially at the MSB codes.
A new “interpolated segmented model” needs to be developed for interpolated DACs.

## Slide 33: Application to various architectures
uSMILE and ER  incorrect DNLs for interpolated DACs especially at the MSB codes.
A new “interpolated segmented model” needs to be developed for interpolated DACs.

## Slide 34: Outline
Conventional linearity testing of DACs
Motivation for segmented testing
uSMILE for DACs
Extrapolated Reconstruction (ER) for DACs
Modifications for Interpolated DACs
Test results

## Slide 35: uISMILE: ultrafast Interpolated Segmented Model Identification of Linearity Errors

## Slide 36: uISMILE: ultrafast Interpolated Segmented Model Identification of Linearity Errors

## Slide 37: ER+I: Extrapolated Reconstruction with Interpolation
Measured voltages
Extrapolated voltages
Measure DAC output for
1 MSB segment (32 codes: 0,1,2,3,…,31) and
MSB points (0,32,64,….,4032,4064)
with multiple hits for each code
“Extrapolate” and “Reconstruct” output curve while accounting for interpolation
Subtract from end-point/best fit line and calculate INLs and DNLs
Example: 12-bit interpolated DAC with 7-5 segmentation
Notes: For equivalent accuracy, total number of samples are equal for uSMILE and ER

## Slide 38: Simulation results for interpolated DAC
INL simulation results of the 16b interpolated DAC
(a) INL estimations using the different methods
(b) Zoomed in view of the INL plots

## Slide 39: Simulation results for interpolated DAC
DNL simulation results of the 16b interpolated DAC
(a) DNL estimations of the 16b DAC using the different methods
(b) Zoomed in view of the DNL plots

## Slide 40: Simulation results for interpolated DAC
DNL simulation results of the 16b interpolated DAC
(a) DNL estimations of the 16b DAC using the different methods
(b) Zoomed in view of the DNL plots

## Slide 41: Simulation results for interpolated DAC
DNL simulation results of the 16b interpolated DAC
(a) DNL estimations of the 16b DAC using the different methods
(b) Zoomed in view of the DNL plots

## Slide 42: Simulation results for interpolated DAC
DNL simulation results of the 16b interpolated DAC
(a) DNL estimations of the 16b DAC using the different methods
(b) Zoomed in view of the DNL plots

## Slide 43: Simulation results for interpolated DAC
DNL simulation results of the 16b interpolated DAC
(a) DNL estimations of the 16b DAC using the different methods
(b) Zoomed in view of the DNL plots

## Slide 44: Simulation results for interpolated DAC
DNL simulation results of the 16b interpolated DAC
(a) DNL estimations of the 16b DAC using the different methods
(b) Zoomed in view of the DNL plots

## Slide 45: Simulation results for interpolated DAC
DNL simulation results of the 16b interpolated DAC
(a) DNL estimations of the 16b DAC using the different methods
(b) Zoomed in view of the DNL plots

## Slide 46: Simulation results for interpolated DAC
DNL simulation results of the 16b interpolated DAC
(a) DNL estimations of the 16b DAC using the different methods
(b) Zoomed in view of the DNL plots

## Slide 47: Simulation results for interpolated DACs
Robustness test for 16b interpolated DACs
INL correlation
DNL correlation

## Slide 48: Outline
Conventional linearity testing of DACs
Motivation for segmented testing
uSMILE for DACs
Extrapolated Reconstruction (ER) for DACs
Modifications for Interpolated DACs
Test results

## Slide 49: Measurement results for an interpolated DAC
Production mixed-signal IC
12b interpolating DAC measured by an on-chip higher resolution internal ADC
12b DAC: m-n segmentation, with interpolation between the output voltages of an m-bit MSB DAC.
“Reference” INL estimation: 240 measurements per code averaged across 10 runs (2400 effective hits per code) to get rid of thermal and flicker noise
Notes: “True” in measurement not possible. Call it reference – explain how it’s obtained

## Slide 50: Measurement results for an interpolated DAC
INL Measurement results for DAC-1
(a) INL estimations using the different methods
(b) Zoomed in view of the INL plots
Notes: “True” in measurement not possible. Call it reference – explain how it’s obtained

## Slide 51: Measurement results for an interpolated DAC
DNL Measurement results for DAC-1
(a) DNL estimations using the different methods
(b) Zoomed in view of the DNL plots
Notes: “True” in measurement not possible. Call it reference – explain how it’s obtained

## Slide 52: Measurement results for an interpolated DAC
DNL Measurement results for DAC-1
(a) DNL estimations using the different methods
(b) Zoomed in view of the DNL plots
Notes: “True” in measurement not possible. Call it reference – explain how it’s obtained

## Slide 53: Measurement results for an interpolated DAC
DNL Measurement results for DAC-1
(a) DNL estimations using the different methods
(b) Zoomed in view of the DNL plots
Notes: “True” in measurement not possible. Call it reference – explain how it’s obtained

## Slide 54: Measurement results for an interpolated DAC
DNL Measurement results for DAC-1
(a) DNL estimations using the different methods
(b) Zoomed in view of the DNL plots
Notes: “True” in measurement not possible. Call it reference – explain how it’s obtained

## Slide 55: Measurement results for an interpolated DAC
DNL Measurement results for DAC-1
(a) DNL estimations using the different methods
(b) Zoomed in view of the DNL plots
Notes: “True” in measurement not possible. Call it reference – explain how it’s obtained

## Slide 56: Measurement results for an interpolated DAC
DNL Measurement results for DAC-1
(a) DNL estimations using the different methods
(b) Zoomed in view of the DNL plots
Notes: “True” in measurement not possible. Call it reference – explain how it’s obtained

## Slide 57: Measurement results for an interpolated DAC
DNL Measurement results for DAC-1
(a) DNL estimations using the different methods
(b) Zoomed in view of the DNL plots
Notes: “True” in measurement not possible. Call it reference – explain how it’s obtained

## Slide 58: Measurement results for an interpolated DAC
DNL Measurement results for DAC-1
(a) DNL estimations using the different methods
(b) Zoomed in view of the DNL plots
Notes: “True” in measurement not possible. Call it reference – explain how it’s obtained

## Slide 59: Measurement results for an interpolated DAC
INL and DNL measurement results for DAC-2

## Slide 60: Measurement results for an interpolated DAC
INL and DNL measurement results for DAC-3

## Slide 61: Measurement results for an interpolated DAC
INL estimation good for all methods
DNL estimation clearly better with uISMILE and ER+I over uSMILE and ER for the interpolated DAC
DNL specs usually stringent (commonly +/-1 LSB)
Theoretical tsf = 20 as compared to conventional method (240 hpc)
Actual total test time reduction (data acquisition + on-chip computation) = ~19.8x for ER+I and ~16x for uISMILE

## Slide 62: Measurement results for an interpolated DAC
Probe data (~30,000 units) : INL
Origin not at 0
y=x+/- tol

## Slide 63: Measurement results for an interpolated DAC
Probe data (~30,000 units) : DNL
Origin not at 0
y=x+/- tol

## Slide 64: Discussion: Difference from major carrier test:
Major carrier test bit-by-bit segmentation
The segmented model “over-parameterizes”
Major carrier test  Cannot capture nonlinearity due to sources other than fixed mismatches
  ex: voltage coefficients, buffer non-ideality etc.
Segmented model  captures non-discontinuous nonlinearities because it gets absorbed into the eM errors
Rule of thumb: Choose more number of MSB bits

## Slide 65: Discussion: ER/ER+I vs uSMILE/uISMILE
ER/ER+I : Multiple measurements at same code  no need to wait after initial settling
ER/ER+I : Data processing extremely simple. Fast and memory efficient
uSMILE/uISMILE:
  Although huge matrix inversions involved, since H matrix depends on input codes, Hinv can be precomputed
  No matrix inversion calculations required, so heavily simplified
  Sequential processing required to get time and memory efficiency == ER/ER+I

## Slide 66: Discussion: ER/ER+I vs uSMILE/uISMILE
uSMILE/uISMILE:
  Potential to catch sparkle INLs (sanity check on noisy errors)
  Segmented INL model + ROME  fast DAC testing with low-linearity digitizers  uSMILE-ROME [3]
  INL model can easily be modified to account for different architectures and nonlinearities
Notes: Inl model modification – alternate flipping between msb voltages

## Slide 67: Conclusion
Novel linearity testing methods that significantly reduce test time have been discussed for DACs with various architectures.
uSMILE and ER  significant time savings for normal segmented DACs
uISMILE and ER+I  significant time savings for interpolated segmented DACs
16b DAC simulation results: >100x time savings
12b DAC measurement results: ~20x time savings
Notes: Contact your topic coordinator if you have any questions. Please route any comments on this slide guide to artdowney@cruzio.com

## Slide 68: References
[1] Z. Yu and D. Chen, “Algorithm for dramatically improved efficiency in ADC linearity test,” in 2012 IEEE International Test Conference, 2012, pp. 1–10.
[2] W. Kester and Analog Devices, inc, Eds., Data conversion handbook. Amsterdam ; Boston: Elsevier ; Newnes, 2005.
[3] S. K. Chaganti, T. Chen, Y. Zhuang, and D. Chen, “Low-cost and accurate DAC linearity test with ultrafast Segmented Model Identification of Linearity Errors and Removal Of Measurement Errors (uSMILE-ROME),” in 2018 IEEE International Instrumentation and Measurement Technology Conference (I2MTC), 2018, pp. 1–6.

## Slide 69
Thank You!
Questions?