## Slide 1: Chopper-stabilized Op Amp Design
Chongli Cai
11/2015

## Slide 2: What is Chopper-stabilized Amp?
Firstly published by TI in 2006 [1]
Goal is to achieve μV offset and extremely low offset drifts for high gain/precision applications.
It turns the polarity of offset constantly so that the average offset is small
[1]Burt, R.; Zhang, J., "A Micropower Chopper-Stabilized Operational Amplifier using a SC Notch Filter with Synchronous Integration inside
the ContinuousTime Signal Path,“in Solid-State Circuits Conference, 2006. ISSCC 2006. Digest of Technical Papers. IEEE International ,
vol., no., pp.1388-1397, 6-9 Feb. 2006

## Slide 3: Basic of Chopping
Figure. 1 Chopping amplifier in unity gain configuration
Figure. 2 Chopping timing diagram
Figure. 3 Frequency domain signal plot
Blue: Vin
Red: Vout
Notes: DC offset gets translated to chopping frequency ().
Chopper is a simple mixer implemented using cross-coupled switches
The signal is unaffected overall at the end of chopping
DC offset gets translated to chopping frequency (𝑓_𝑐ℎ𝑜𝑝).
Chopper is a simple mixer implemented using cross-coupled switches
The signal is unaffected overall at the end of chopping

## Slide 4: Basic Architecture of CHS Amp
Input stage Offset of high-gain path directly contributes to the overall offset voltage
Input stage of high-gain path requires to be chopped.
Multipath Nested Miller Compensation (MNMC) is applied for stabilization
High-speed path
High-gain path
Two-stage

## Slide 5: Frequency Compensation (MNMC)
LF
HF
The stitching frequency is defined as
Pole-zero cancellation needs to be precision controlled for fast transient
Chopping frequency needs to be selected higher than pseudo-static BW

## Slide 6: Frequency Compensation (MNMC)
The notch filter in ripple reduction loop can introduce “unclear” roll-off, which can degrade the stability & settling performance.
Put the fchop higher than stitching frequency can avoid this

## Slide 7: Top Level

## Slide 8: Input Chopper Switch
Input chopper is directly connected to the amplifier’s input
It needs to support rail-to-rail input CM range => bootstrapped
The switch size needs to be carefully determined in terms of noise

## Slide 9: Input Chopper – with bootstrap
Vcm detector
ɸ0 & ɸ1 are two complementary clocks
ɸ0F & ɸ1F are chopper switches
gate control clocks, which have voltage
levels dependent on Vcm of inputs
Input CM voltage VssF is generated
by Vcm detector circuit
All transistors are isolated transistors
Chopper Switches
ac-coupled Level shift
Switches’ Ron need
constant through ICMR

## Slide 10: Top Level

## Slide 11: Output Chopper
Output chopper & chopper in the RRL are less critical than input chopper
The switches are not required to be bootstrapped because the voltage
variation at first stage output is small.

## Slide 12: Top Level
Down-modulated Vos back to DC to compensate Initial offset.
Up-modulated Vin & offset of gm3 are filtered
Notch filter is used to filter out signal at fchop

## Slide 13: Ripple Reduction Loop
Switched-capacitor based notch filter
is used
Notch filter clock signal has 90 degree
phase shift with chopping clock.
DC input @ gm3 becomes modulated
Current flowing into input of NF and then
Integrated by sampling caps.
The signal is only sampled when it
crosses zero due to orthogonal CLK
Orthogonal clock
Kusuda, Y., "Auto Correction Feedback for Ripple Suppression in a Chopper Amplifier,"
in Solid-State Circuits, IEEE Journal of , vol.45, no.8, pp.1436-1445, Aug. 2010

## Slide 14: Orthogonal Clock Generation

## Slide 15: Gain stages
Monticelli
output stage
With cascode stage
Folded-cascode
gain stage
Folded input pair

## Slide 16: Gm1 (folded-cascade in HG path)
RRL current adding here
Connect to input chopper
Connect to input chopper

## Slide 17: gm0
Connect to the cascode
Stage before output stage

## Slide 18: A3
Cascode stage
Output stage
NMOS pair
PMOS pair

## Slide 19: gm2

## Slide 20: Design Steps
Design the 3-stage amplifier with MNMC
Simulate its AC performance (GBW, UGF, PM), transient performance (SR. settling time) and noise
Design ripple reduction loop (RRL)
Add the RRL to the amp with ideal I/O choppers
Run transient simulation to verify amp output can settle into a steady-state and offset ripple is small enough (<5µV)
Design input/output choppers
Replace the ideal chopper with real one in the amp
Run transient simulation to ensure the amp output can settle into a steady-state and offset ripple is small (<5µV)
Run PAC/ Pnoise to verify the ac and noise performance with chopping on

## Slide 21: Simulation Test-bench - offset
Offset voltage
Setting the Vicm at sweet spot of the input common mode range
Run the transient simulation and plot (Vo - Vicm)

## Slide 22: Simulation Results - Vos
Average OS= 663.4nV with 1.1mV(3σ) initial OS
glitch
Offset is calculated by clipping the waveform after settled
and taking the average value.
Clip range for aver Vos Cal

## Slide 23: Offset Ripple
Offset ripple

## Slide 24: Simulation Test-bench – AC/Noise
PAC / Pnoise
Setting the Vicm at sweet spot of the input common mode range
Run PSS/PAC/Pnoise simulation

## Slide 25: PAC Simulation

## Slide 26: Pnoise

## Slide 27: Simulation Test-bench - transient
transient simulation is used to verify the start-up of the op-amp, SR, settling time
and ripple reduction loop stability.

## Slide 28: RRL Stability Simulation
Notch Filter Output
Op-amp start-up

## Slide 29: Simulation Test-bench - ICMR
ICMR is measured in terms of Vos.
In this step, we can keep the chopping off and sweep Vicm from rail to rail to find the range where the Vos is keeping near zero (without mismatch)
Another voltage source is used to force the Vo at its sweet spot.

## Slide 30: Simulation Test-bench (AOL)